## Slide 1
This work was funded by the U.S. National Science Foundation under grant EAR 0622374. Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the National Science Foundation.
1
David G. Tarboton1, David R. Maidment2, Ilya Zaslavsky3, Jeffery S. Horsburgh1, Tim Whiteaker2, Michael Piasecki4, Jonathan L Goodall5, David Valentine3, Thomas Whitenack3
Utah Water Research Laboratory, Utah State University, Logan, Utah, USA; 2. Center for Research in Water Resources, University of Texas at Austin, Austin, Texas, USA; 3. San Diego Supercomputer Center, University of California at San Diego, San Diego, California, USA; 4. Department of Civil, Architectural, and Environmental Engineering, Drexel University, Philadelphia, Pennsylvania, USA; 5. Department of Civil and Environmental Engineering, University of South Carolina, Columbia, South Carolina, USA.
http://his.cuahsi.org
Sharing Hydrologic Data with the CUAHSI* Hydrologic Information System
Overview
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.
Data Discovery and Integration platform
Data Publication platform
Data Synthesis and Research platform
Data Services
Metadata Services
Metadata Search
HIS Central
HydroDesktop
HIS Server
Service registration
Catalog harvesting
Service and data theme metadata
Data carts
Water Data Services
Spatial Data Services
Service Oriented Architecture
HIS Server is a repository of hydrologic time series data published as WaterOneFlow web services
HIS Central is a metadata catalog of data accessible through WaterOneFlow web services
Hydro Desktop accesses hydrologic data discovered on HIS Central and acquired from HIS Servers
Like search portals Google, Yahoo, Bing
Like browsers
Like web servers
Like HTML
The three components function for hydrologic information analogously to the internet as a whole comprised of web servers, browsers, and search portals interacting using HTML for text and images
You can participate through establishing a HIS Server to organize and share your data, discovering and accessing data through HydroDesktop and contributing to the open source system development. See http://his.cuahsi.org and http://www.hydrodesktop.org.
H51H-0854
HIS Server
ODM
ODM
ODM
WaterOneFlow
WaterOneFlow
WaterOneFlow
HIS Server
Database
ODM Databases and WaterOneFlow Web Services
ArcGIS Server Spatial Data Services
Spatial
Services
WaterOneFlow
Services
Map Server
Time Series Analyst
HIS Server Website
HIS Server Capabilities Web Service
HIS Server Database Configuration Tool
HIS Server is comprised of a collection of datasets, web services, tools, and software applications that allow data producers to store, publish, and analyze space-time hydrologic datasets
Designed to permit local control of the data, while still being part of a distributed, national/international system allowing universal access to the data
Enables producers of hydrologic data to join a growing, distributed network of published hydrologic data services
Tools for local management of data on the server, as well as a set of Internet-based applications for accessing, visualizing, and downloading hydrologic data
CUAHSI Water Data Services System Components
Base Station
Computer(s)
Telemetry Network
Sensors
Query, Visualize, and Edit data using ODM Tools
Excel, text
ODM
Database
ODM Data Loader
Streaming Data Loader
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
Platform independent Analysis
GIS
Matlab
Splus
R
IDL
Java
C++
VB
Discovery and Access
Hydro
Desktop
HydroExcel
Water Metadata Catalog
Harvester
Service Registry
HIS Central
USGS NWIS
EPA STORET
NCDC
Others
Observations Data Model (ODM)
What are the basic attributes to be associated with each single data value and how can these best be organized?
Streamflow
Flux tower
data
Precipitation
& Climate
Groundwater
levels
Water Quality
Soil
moisture
data
A relational database at the single observation level (atomic model)
Stores observation data made at points
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Standard format for data sharing
Cross dimension retrieval and analysis
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment and I. Zaslavsky, (2008), A Relational Model for Environmental and Water Resources Data, Water Resour. Res., 44: W05406, doi:10.1029/2007WR006392.
Stage and Streamflow in ODM Example
Summary
The CUAHSI Hydrologic Information System provides
Data Storage in an Observations Data Model (ODM) on an HIS Server
Data Delivery through internet-based Water Data Services using a consistent data language, called WaterML
Data Discovery through federated thematic keyword search services and a National Water Metadata Catalog
Data Access and Analysis through a Client Application (HydroDesktop)
1
2
2
3
Query functions
Return data in WaterML
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
OGC process for worldwide standardization
Some adoption by USGS and NCDC
WaterML and WaterOneFlow
3
4
HydroDesktop
Platform for data discovery, access, integration and analysis
Uses MapWindow 6 open source GIS software development toolkit
Plug-in architecture
Data abstraction layer
http://hydrodesktop.codeplex.com open source software development portal
Windows and Mac compatible (through Mono)
Observations
Models
Climate
GIS
Remote Sensing
4
* CUAHSI is the Consortium of Universities for Hydrologic Sciences, Inc. a consortium of 133 University and research organizations with support from the U.S. National Science Foundation to develop infrastructure for hydrologic science research. See http://www.cuahsi.org.
Dynamic controlled vocabulary moderation system
Local ODM
Database
Master ODM Controlled Vocabulary
ODM Website
ODM Controlled
Vocabulary Moderator
ODM Data Manager
ODM
Controlled Vocabulary
Web Services
ODM
Tools
HIS
Server
XML
http://his.cuahsi.org/mastercvreg.html
Reducing Semantic Heterogeneity
1
2