## Slide 1
Study Area
Ibrahim N. Mohammed, David G. Tarboton
Civil and Environmental Engineering, Utah State University, Utah Water Research Laboratory, Logan, UT 84322-4110, nourein@cc.usu.edu
Modeling the Dynamics of the Great Salt Lake as an Integrator of Regional Hydrologic and Climate Processes?
Abstract
The Great Salt Lake (GSL), Utah, is the fourth largest, perennial, terminal lake in the world. The Great Salt Lake (GSL) level fluctuates due to the balance between inflows and outflows. These fluctuations are of interest whether they are high (flooding hazards) or low (economic impacts). Inflows are due to streamflow, primarily from the Bear River (54%), Weber River (18%) and Jordan/Provo River (28%). Inflows also include precipitation directly on the lake and groundwater both from the East and West sides. The only outflow is evaporation that is controlled by the climate, area of the lake that changes with level. The GSL reached historic high levels above 1284 m in 1873 and 1986. A historic low at 1278 m occurred in 1963. These fluctuations represent the integrated effect of climate and hydrologic processes as well as the dynamic interaction between lake volume, area and salinity that impact evaporation from the lake. The topographic area-volume relationship in the GSL plays a role in the system dynamics because area is a control on the evaporation outflux. This paper examines the relationships between Basin climate (precipitation and temperature), Inflows to the lake (primarily streamflow) and outflows (evaporation). The role played by the topographic elevation-area-volume relationship on lake dynamics and the correspondence between modes in volume and area distributions and peaks in the area-volume derivatives was examined. We derived, using a steady state approximation, the relationship between distributions of lake volume and lake area and the area-volume derivative from the topography/bathymetry. This analysis showed that both the topography /bathymetry and multimodality in the area distribution are required to explain the observed multimodality in the volume distribution. We also separated lake volume changes into increases in the spring (due to spring runoff) and declines in the fall (due to evaporation) and then related these volumes changes to streamflow, precipitation, and basinwide climate inputs. The results of this study improve understanding of the sensitivity of the GSL level to the interplay between topography and fluctuations in precipitation and climate and thereby contribute to knowledge on the interactions between hydrologic processes and long-term large-scale climate fluctuations.
Motivation
Primary process interactions in the Great Salt Lake Basin that drive lake volume fluctuations.
The Great Salt Lake Basin with major sub-basins. The Great Salt Lake is located in the north east of the Great Basin (upper left).
Closed Basin that integrates climate and hydrologic inputs over the region.
Fluctuations of the GSL’s level are of direct concern to mineral industries along the shore, the Salt Lake City Airport, the Union Pacific Railroad, and Interstate highway 80.
Flooding. During 1983-1986 the Great Salt Lake rose rapidly to its highest level in a hundred years and then declined quickly. A pumping project that cost about $60 million was initiated due to that event.
Model the changes in GSL volume and fluctuations in GSL level as they are related to the inputs of precipitation, temperature and other regional measures of climate.
Explore the role of the topographic area-volume relationship in the occurrence of modes representing potential preferred states in the system dynamics possibility of relationships between modes in the lake volume distribution and attributes,
Understand the full set of interactions between basin hydrology and lake inputs and outputs.
Objectives
BEAR R
WEBER R
JORDAN R
Air Humidity
Streamflow
Soil Moisture
And
Groundwater
Mountain
Snow pack
Precipitation
Air Temp.
Evaporation
Solar
Radiation
Salinity
GSL Level
Volume
Area
GSL System Conceptual Model
Jordan River
Weber River
Bear River
Bear watershed {19,262 km2}→ Bear River
→average annual flow @ Corinne 1600M m3/year.
Weber watershed (6,413 km2)→ Weber River
→average annual flow @ Plain city 520M m3/year.
Jordan/ Provo watershed (9,963 km2)→ Provo & Jordan Rivers
→ average annual flow @ SLC 1700 South 126M m3/year.
West Desert watershed (14,604 km2) → {no perennial streams}
H41C-0422

## Slide 2
Rise precipitation (m3)
Area (acre 106)
Density
Area (m2 106)
Great Salt Lake (GSL) total volume goes through an annual cycle where on average the lake is rising between November 1 {trough date} and June 15 {peak date}, and falls from June 15 to November 1. (Frequency Domain Analysis)
Rise (ΔV+) = GSL total volume on June 15th @ yeari+1- GSL total volume on November 1st @ yeari [i refers to the year of the beginning period].
Fall (ΔV-) = GSL total volume on November 1st @ yeari- GSL total volume on June 15th @ yeari .
Climate Inputs (Maurer et al., 2002).
km3
Acre-Feet  107
Great Salt Lake Levels from USGS.
GSL Bathymetry Relations, (Loving et al., 2000).
Volume (km3)
Volume (km3)
Area (km2)
Level (meter)
Level (meter)
Area (km2)
I
Mass Balance:
I = Inflow (Precipitation + Streamflow) [L3/T]
E = Evaporation [L/T]
A = Area [L2]
V = Volume [L3]
Where;
A
E
V
Lake x-section
Steady State:
I,E
A
Bathymetry:
V
f(I)
f(A)
f(V)
f(E)
Bathymetry
fI(i)
fA(a)
Mass Balance
Bathymetry
fV(v)
The probability density function (PDF) of V is related to the rate of change of A with V, (expressed as a derivative) and this analysis suggests that both modes in the PDF of A & peaks in the derivative dA/dV should adjust each other to produce the modes in the probability density function of V.
Observed fA(a) with Constant dA/dV,
fA(a) a normal distribution with observed dA/dV,
Observed fA(a) with observed dA/dV.
fV(v) is examined sensitively to bathymetry described by dA/dV by the following;
Method & Results
Spectral Analysis
Log (|A|)
Biweekly volume (1979-2000)
V km3
V+
V-
June 15th
Reconstructed GSL Annual cycle - Peak June 15, Trough Nov 1.
Fourier Transform
Month
Nov. 1st
Annual Increase & Decrease
V (+ or -) m3
June 15 - Nov 1
Nov 1 - June 15
References
Lall, U., T. Sangoyomi and H. D. I. Abarbanel, (1996), "Nonlinear Dynamics of the Great Salt Lake: Nonparametric Short Term Forecasting," Water Resources Research, 32(4): 975-985.
Loving, B. L., K. M. Waddell and C. W. Miller, (2000), "Water and Salt Balance of Great Salt Lake, Utah, and Simulation of Water and Salt Movement through the Causeway, 1987-98," Water-Resources Investigations Report, 00-4221, U.S. Geological Survey, Salt Lake City, Utah, p.32, 2000.
Maurer, A.W. Wood, J.C. Adam, D. P. Lettenmaier and B. Nijssen, (2002), "A Long-Term Hydrologically Based Dataset of Land Surface Fluxes and States for the Conterminous United States," Journal of Climate, 15(22): 3237-3251.
GSL & Bear River Basin Empirical Relationships
Data
Acre-feet
Multimodality observed in biweekly lake volumes 1847-1992, (Lall et al., 1996).
GSL watersheds streamflows (Nov-Jun)
m3
GSL biweekly volumes. Separate records for the north & south arms are available since 1966.
Volume (acre-feet)
Density
Observed fA(a(V))  Observed dA/dV
Normal fA(a(V))  Observed dA/dV
Observed fA(a(V))  Constant dA/dV
Observed fV(v)
Volume (km3)
Area Density Function (1847-2004)
meter
feet
Rise streamflow (m3)
Line 1:1
dV(+) ( m3)
(2)
(1)
The role of topography/bathymetry in the lake dynamics and the occurrence of modes in the volume distribution:
Modeling the changes of GSL volume :
Multimodality in the lake volume is due to both inputs (as inferred from area) and bathymetry through dA/dV.
Bathymetry through dA/dV modulates to the pdf of the lake volumes.
Multimodality in the lake volume is due to both inputs (as inferred from area) and bathymetry through dA/dV.
Streamflow is dominate for GSL volume,
Evaporation in GSL is area control,
Air temperature increases Evaporation,
Air temperature reduces Mountain snowpack,
Mountain snowpack supplies Streamflow,
Precipitation contributes to GSL volume.
Conclusions
(2)
(1)
Evaporation (m3)
dV(-) ( m3)
EGSL = PGSL+QGSL-VGSL
LOWESS
(R defaults)
dV(+) ( m3)
Area (m2)
Evaporation ( m3)
Ev/A (m)
Area (m2)
Ev/A (m)
Temperature (˚C)
Rise precipitation (m)
Bear watershed
Q/A @ Corinne (m)
Temperature (˚C)
Q/A @ Corinne (m)
Bear watershed