## Slide 1
This research was funded by the US Army Research and Development Center under contract number W9124Z-08-P-0420
H41A-0867
Overview
1
Hydrologic terrain analysis augments the information content of digital elevation data by removing spurious pits, defining a connected flow field, and calculating surfaces of hydrologic information derived from the flow field. It supports watershed delineation and preprocessing for distributed hydrologic models. This work advances the capability to derive hydrologic information from digital elevation data using parallel programming methods to provide improved runtime efficiency and enable the capability to run larger problems.
6
4
David G Tarboton1, Dan W Watson2, Robert M Wallace3, Kim A T Schreuders1, Teklu Tesfa1
1. Utah Water Research Laboratory, Utah State University, Logan, Utah, USA, 2. Computer Science, Utah State University, Logan, Utah, USA,
3. US Army Engineer Research and Development Center, Information Technology Lab, Vicksburg, Mississippi, USA
http://www.engineering.usu.edu/dtarb/taudem
2
5
Overall Parallel Approach
Hydrologic Terrain Processing Using Parallel Computing
MPI, distributed memory paradigm
Row oriented partitions
Each process includes one buffer row on either side
Each process does not change buffer row
Each process uses block input/output on its part of the domain
Each process does as much as it can within its domain before sharing information across borders
3
Pit Removal
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM
Initialization
1st Pass
2nd Pass
Planchon, O., and F. Darboux (2001), A fast, simple and versatile algorithm to fill the depressions of digital elevation models, Catena(46), 159-176.
Parallel Algorithm
Swap Borders
Initialize( D,P) Do for all i in S (or all cells on first pass) if D(i) > n P(i) ← D(i) Else P(i) ← n Add i to S for next pass endfor Send( topRow, rank-1 ) Send( bottomRow, rank+1 ) Recv( rowBelow, rank+1 ) Recv( rowAbove, rank-1 ) Until P is not modified
D denotes the original elevation.
P denotes the pit filled elevation.
S denotes process stack
n denotes lowest neighboring elevation
i denotes the cell being evaluated
Efficiency features
A pair of last on first off stacks is used to from second iteration on only examine cells with altered elevation
Alternating directions enhance convergence
Swap Borders
Pit Remove Block versus Cell read grid read times for GSL 100
Timing Analysis Results
Test Datasets
GSL100
4045 x 7402 = 29.9 x 106 cells  120 MB
Pit Remove Compute time for Domain versus Stack iteration, GSL100
Stripe partitioning approach has enabled the parallelization of key terrain analysis functions resulting in significant speed up and capability to process larger grids
Parallel PitRemove yielded a total speed up of a factor of ~ 6 using 8 processors compared to the ArcGIS Pit Remove. Of this a factor ~ 2 appeared to be due to the algorithm and a factor of ~ 3 due to use of 8 processors
Incremental improvements during development were due to
  Block read speed up ~ factor 100
  Stack iteration speed up ~ factor 2
  Future Work
  Work is ongoing to implement a parallel version of the complete TauDEM tool set
  Tiled grid files to address file size limitations
  Carving and optimal pit removal in addition to pit removal by filling
Pit Remove Total and Compute time, GSL100
Pit Remove Total and Compute time, NedGridB
Computer Specifications: 64 bit Dual Quad Core Xeon Proc E5405, 2.00GHz.
3 x 1 TB disks, Raid 5. Windows Server 2008. $5,000.
Extends flow accumulation approaches commonly available in GIS through the integration of multiple inputs and a broad class of algebraic rules into the calculation of flow related quantities.
Based on establishing a flow field through DEM grid cells, that is then used to evaluate any mathematical function that incorporates dependence on values of the quantity being evaluated at upslope (or downslope) grid cells as well as other input quantities.
Generalized Flow Algebra
r
c
qi
qk
D multiple flow direction model
D
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
Pki
Pki
Pki
i
Grid flow field Pki
i = FA(i, Pki, k, k)
Evaluation of general function based on upslope or downslope quantities
A quantity  is evaluated at grid cell i as a function of the same quantity at upslope grid cells, the flow field defined in terms of proportions Pki of flow from cell k to cell I, and other inputs  at cell i and neighbor cells k.
No loops
Example: Retention limited runoff generation with run-on
<1 ha
1-4 ha
4-8 ha
>8 ha
Contributing area
Parallel Evaluation of Contributing Area/Flow Algebra
Executed by every process with grid flow field P, grid dependencies D initialized to 0 and an empty queue Q. FindDependencies(P,Q,D) for all i for all k neighbors of i if Pki>0 D(i)=D(i)+1 next k if D(i)=0 add i to Q next
Executed by every process with D and Q initialized from FindDependencies. FlowAlgebra(P,Q,D,,) while Q isn’t empty get i from Q i = FA(i, Pki, k, k) for each downslope neighbor n of i if Pin>0 D(n)=D(n)-1 if D(n)=0 add n to Q next n end while swap process buffers and repeat
Building the dependency grid
Flow algebra function
Dependency grid is used to track the number of unevaluated upslope grid cells within each partition
Grid cells with zero dependencies placed on separate evaluation queue for each process
Sharing between processes when queue’s are empty and iteration until all done
NedGridB
14849 x 27174 = 403.3 x 106 cells  1600 MB
7
Conclusions
D-infinity Contributing Area Total and Compute time, GSL100
8
Dependencies & Limitations
MPICH2 library from Argonne National Laboratory
http://www.mcs.anl.gov/research/projects/mpich2/
TIFF (GeoTIFF) 4 GB file size
Processor memory (especially limiting on 32 bit systems)