## Slide 1: GIS, Hydrology and Terrain Analysis Using Digital Elevation Models
David G. Tarboton
dtarb@cc.usu.edu
http://www.engineering.usu.edu/dtarb

## Slide 2: Overview
GIS as a tool for Hydrologic Modeling
The ArcGIS Hydrology Model
Terrain Analysis Using Digital Elevation Models. (Some new Spatial Concepts)
Extendability of ArcGIS (TauDEM as an example)
Demonstration of TauDEM

## Slide 3: Grey River, New Zealand South Island
Subwatershed attributes
Stream segment attributes
Basin Area: 3817 km2
Flow: 12.1 x 109 m3
Flow/Area: 3184 mm
Christchurch
Greymouth
"Data based on contours supplied by Land Information New Zealand"
TOPNET Model
Notes: Much of hydrology is spatial, so GIS provides a natural tool for Hydrologic Modeling. This slide illustrates the development of Hydrologic Model information from GIS.

## Slide 4: Rainfall interpolation and adjustment
Notes: Complicate slide, but bear with me as I explain it because rainfall estimation is a crucial problem here. Wanted to model the spatial pattern of rainfall over the watershed, recognizing orographic variability and using the gauges present
Circles show rain gauges.
The contours show the estimate of the mean annual rainfall surface that reflects the orographic effects. The surface was constructed by Roddy Henderson using what he had learnt from doing rainfall-runoff data analysis for many West Coast catchments. He assumed that the upper envelope of measured annual rainfall along each NW->SE path was the best estimate of the actual rainfall process. By doing this, he discounted lower measurements on the grounds that they were perhaps only representative of very local conditions (~1 km), and did not necessarily constitute a representative sample for spatial interploation purposes.
2. By constructing envelope curves for many NW->SE paths on the West Coast, Roddy inferred the location and magnitude of the annual rainfall peak(s). For the Grey, there are peaks slightly
upwind of both the Paparoa Ranges and Southern Alps.
3. He generalised his envelope by fitting a simple surface to it. (I think the rain surface was constrained so that the peak rain along any NW-SE path across the catchment was 12 m/yr. If there were two peaks along a path, then the sum of the peaks was 12 m/yr.) Rain was distributed along each path by assuming an exponential fall-off from the peak(s). The rainfall at sea level on the West Coast, and on the Canterbury Plains was taken to be the observed amounts, since orography does not affect these sites greatly.
Need precipitation at each point as a weighted average of precipitation from nearby weights. Used a scheme to determine weights based upon Delauney triangles, linear interpolation and normalization by annual rainfall estimate.

## Slide 5: Parameters
Hydraulic conductivity K, calibrated using multiplying factor applied to spatially variable values.
The soil capacity parameter ‘soilc’ is estimated as (soil zone depth)/(dth1+dth2)
Spatially variable
Spatially constant

## Slide 6: Basin average precipitation
Streamflow at outlet
Cumulative water balance

## Slide 7
“White space” is the Grey at Dobson minus Ahaura, Arnold and Grey at Waipuna

## Slide 8: SINMAP
Terrain Stability Mapping

## Slide 9: Flood Plain Mapping
ArcView
Digital
Elevation
Model
HEC-HMS
Flood
discharge
HEC-RAS
Water
surface
profiles
ArcView
Flood
plain maps
CRWR-PrePro
AvRAS
Digital Map Database
Slide from David Maidment, University of Texas at Austin.

## Slide 10: HMS Schematic Prepared with CRWR-PrePro
Mansfield Dam
Colorado
River
Slide from David Maidment, University of Texas at Austin.

## Slide 11: HMS Results
Watershed 155
Junction 44
Slide from David Maidment, University of Texas at Austin.

## Slide 12
Map-Based Surface Water Runoff
Estimating the surface water yield
by using a rainfall-runoff function
Runoff, Q
(mm/yr)
Precipitation, P
(mm/yr)
Accumulated Runoff
(cfs)
P
Q
Runoff Coefficient
C = Q/P
Slide from David Maidment, University of Texas at Austin.

## Slide 13: Water Quality: Pollution Loading Module
DEM
Precip.
Runoff
LandUse
EMC Table
Concentration
Load
Accumulated
Load
Load [Mass/Time] = Runoff [Vol/Time] x Concentration [Mass/Vol]
Slide from David Maidment, University of Texas at Austin.

## Slide 14: GIS in Water Resources Consortium
Bringing together these two communities by using a common geospatial data model
http://www.crwr.utexas.edu/giswr
GIS
Water Resources
CRWR
Slide from David Maidment, University of Texas at Austin.

## Slide 15: ArcGIS Data Models
Facilitate a process with the user community
Capture the essential, common data model for each discipline
Build a database design template that works well with ArcGIS
Build on experience, not a standards exercise
Share the model on ArcOnline
http://arconline.esri.com/arconline/datamodels.cfm
Slide from David Maidment, University of Texas at Austin.

## Slide 16: Essential Data Model
Organization A
Organization B
Organization D
Organization C
Something in common
The data model for a business organization tends not to change greatly over time unless the business organization changes the fundamental way that it does business
Slide from David Maidment, University of Texas at Austin.

## Slide 17
ArcGIS Hydro Data Model
Flow
Time
Time Series
Hydrography
Network
Channel
Drainage
HydroFeatures
Slide from David Maidment, University of Texas at Austin.

## Slide 18
Slide from David Maidment, University of Texas at Austin.

## Slide 19: Elevation Surface — the ground surface elevation at each point
Digital Elevation Model — A digital representation of an elevation surface. Examples include a (square) digital elevation grid, triangular irregular network, set of digital line graph contours or random points.
Terrain Analysis Using Digital Elevation Models

## Slide 20: Digital Elevation Grid — a grid of cells (square or rectangular) in some coordinate system having land surface elevation as the value stored in each cell.
Square Digital Elevation Grid — a common special case of the digital elevation grid

## Slide 21: Digital Elevation Model Based Flow Path Analysis
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
3
3
12
2
2
2
3
16
25
6
Drainage Area
4
5
6
3
7
2
1
8
Eight direction pour point model D8
Grid network
D

## Slide 22: Topographic Slope
?
Topographic Definition Drop/Distance
Limitation imposed by 8 grid directions.
Flow Direction Field — if the elevation surface is differentiable (except perhaps for countable discontinuities) the horizontal component of the surface normal defines a flow direction field.

## Slide 23
The D Algorithm
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)
D Flow Direction Grid — A special case of a multiple flow direction grid in which the flow direction is represented by an angle stored in each grid cell

## Slide 24
Contributing Area using D8
Contributing Area using D

## Slide 26
Useful for example to track where sediment or contaminant moves

## Slide 27
Useful for example to track where a contaminant may come from

## Slide 28
Reverse Accumulation
Useful for destabilization sensitivity in landslide hazard assessment

## Slide 29: Transport limited accumulation
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment

## Slide 30: Drainage area can be concentrated or dispersed (specific catchment area)

## Slide 31: Specific catchment area a is the upslope area per unit contour length [m2/m  m]
Upslope contributing area a
Stream line
Contour line
Topographic Definition

## Slide 32
Contributing Area — a field representing at each point the magnitude of the drainage area upslope of that point. Also called Catchment Area, Drainage Area or Flow Accumulation.
Specific Catchment Area — a field representing contributing area per unit contour width. Units are length.
Concentrated Contributing Area — the contributing area on a smooth surface or flow line where surface flow has concentrated and there is a measurable contributing area to a point. Units are area.
Contributing Area Grid — a grid derived from the flow direction grid, which counts in each cell the number of upstream cells draining through that cell.

## Slide 33: Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and delineate model elements that account for this.
Concentrated versus dispersed flow.
Objective delineation of channel networks using digital elevation models.

## Slide 34: How to decide on drainage area threshold to determine channels and watershed model elements?
500 cell theshold
1000 cell theshold

## Slide 35: Topographic Texture and Drainage Density
Same scale, 20 m contour interval
Sunland, CA
Driftwood, PA

## Slide 36: Strahler Stream Order Stream Drop: Elevation difference between ends of stream
Note that a “Strahler stream” comprises a sequence of links (reaches or segments) of the same order
Nodes
Links
Single Stream
most upstream is order 1
when two streams of a order i join, a stream of order i+1 is created
when a stream of order i joins a stream of order i+1, stream order is unaltered

## Slide 37: Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
Look for statistically significant break in constant stream drop property
Break in slope versus contributing area relationship
Physical basis in the form instability theory of Smith and Bretherton (1972), see Tarboton et al. 1992

## Slide 38: Statistical Analysis of Stream Drops
Stream drop test for Mawheraiti River. For each upward curved support area threshold the stream drop for each stream is plotted against Strahler stream order. The large circles indicate mean stream drop for each order The weighted support area threshold, drainage density (in km-1) and t statistic for the difference in means between lowest order and all higher order streams is given.
Threshold = 10
Dd = 2.5
t = -3.5
Threshold = 15
Dd = 2.1
t = -2.08
Threshold = 20
Dd = 1.9
t = -1.03

## Slide 39
Curvature based stream delineation with threshold by constant drop analysis

## Slide 40: Why Programming

## Slide 41: TauDEM Software Functionality
Pit removal (standard flooding approach)
Flow directions and slope
  D8 (standard)
  D (Tarboton, 1997, WRR 33(2):309)
  Flat routing (Garbrecht and Martz, 1997, JOH 193:204)
Drainage area (D8 and D)
Network and watershed delineation
  Support area threshold/channel maintenance coefficient (Standard)
  Combined area-slope threshold (Montgomery and Dietrich, 1992, Science, 255:826)
  Local curvature based (using Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
Threshold/drainage density selection by stream drop analysis (Tarboton et al., 1991, Hyd. Proc. 5(1):81)
Wetness index and distance to streams

## Slide 42: TauDEM Software Architecture
ESRI binary
grid
ASCII text
grid
ESRI gridio API
(Spatial analyst)
USU TMDLtoolkit modules
(grid, shape, image, dbf, map, mapwin)
TauDEM C++ library
Fortran (legacy)
components
Standalone
command line
applications
C++ COM DLL interface
VB GUI
application
ESRI ArcGIS 8.1
(Toolbar under
development )
Vector shape
files
Data
formats
Available from
http://www.engineering.usu.edu/dtarb/
Binary direct
access grid

## Slide 43
Implementation Details
Spatial Analyst includes a C programming API (Application Programming Interface) that allows you to read and write ESRI grid data sets directly.
Excerpt from gioapi.h
/ * GetWindowCell - Get a cell within the window for a layer,
* Client must interpret the type of the output 32 Bit Ptr
* to be the type of the layer being read from.
*
* PutWindowCell - Put a cell within the window for a layer.
* Client must ensure that the type of the input 32 Bit Ptr
* is the type of the layer being read from.
*
*/
int GetWindowCell(int channel, int rescol, int resrow, CELLTYPE *cell);
int PutWindowCell(int channel, int col, int row, CELLTYPE cell);

## Slide 44
STDMETHODIMP CtkTauDEM::Areadinf(BSTR angfile, BSTR scafile, long x, long y, int doall, BSTR wfile, int usew, int contcheck, long *result)
{
USES_CONVERSION; //needed to convert from BSTR to Char* or String
*result = area( OLE2A(angfile), OLE2A(scafile), x,y,doall, OLE2A(wfile),
usew, contcheck);
return S_OK;
}
C++ COM Methods used to implement functionality using Microsoft Visual C++

## Slide 45: Visual Basic for the GUI and ArcGIS linkage
Private TarDEM As New tkTauDEM
…
Private Function runareadinf(Optional toadd As Boolean = False) As Boolean
Dim i As Long
runareadinf = False
i = TarDEM.Areadinf(tdfiles.ang, tdfiles.sca, 0, 0, 1, "", 0, 1)
If TDerror(i) Then Exit Function
If toadd Then
AddMap tdfiles.sca, 8
End If
runareadinf = True
End Function

## Slide 46: GIS in Water Resources Online
A Virtual Course Presented On-Line by David Maidment at the University of Texas at Austin in partnership with Utah State University. Next offering Fall 2002.
Goals:
  To teach the principles and operation of geographic information systems, focusing in particular on ArcView and its Spatial Analyst extension.
  To show how spatial hydrologic modeling can be done by developing a digital representation of the environment in the GIS, then adding functions simulating hydrologic processes.
  To develop individual experience in the use of GIS in Water Resources through execution of a term project, and presenting it both orally and written form in html on the world wide web.
http://moose.cee.usu.edu/giswr/

## Slide 47: Demonstration