## Slide 1: Salinity, Evaporation and the Rise and Fall of the Great Salt Lake
DAVID G. TARBOTON
IBRAHIM N. MOHAMMED

## Slide 2: Great Salt Lake Hydrology
Terminal lake with inflow from 3 major rivers to east.
Only outflow is evaporation.
Lake level and area fluctuates dynamically to adjust outflow to inflow.
Lake volume impacts salinity (dilution).
Salinity impacts evaporation (saturation vapor pressure)
Lake levels are important for infrastructure, industry and commerce near and on the lake

## Slide 3
From http://www.doi.gov/water2025/index.html
The availability of water to sustain life is perhaps the most recurrent constraint in human history and will remain so in the foreseeable future.

## Slide 4: The Great Salt Lake Basin
Bear
West Desert
Jordan/Provo
Weber
Strawberry
A microcosm for many Western Water Issues
Notes: Here is the perspective from 50 miles up. The Great Salt Lake basin is a place of contrast, typical of much of the semi-arid west. Snow is a driver hydrologically. The lake is an integrator. Growth induces change that is important to understand.
Climate Gradients (Snow fed, Alpine to semi-arid), variability and vulnerability
Topographic and Land Use Gradients
Mountain Front / Valley groundwater dynamics and interactions
Geologic Diversity (Granite to Karst)
Closed basin for water and constituent balance closure
Development issues (local growth, SLC metropolitan area demands)
Policy Issues (3 states)
Agricultural issues (water supply, environmental compliance)
Environmental Issues (water quality, watershed management practices)
Ecological issues (Stream ecosystems, Bird refuge, GSL ecosystem)

## Slide 5: A microcosm for many "western" water issues
Climate Gradients (Snow fed, Alpine to semi-arid), variability and vulnerability
Topographic and Land Use Gradients
Mountain Front / Valley groundwater dynamics and interactions
Geologic Diversity (Granite to Karst)
Closed basin for water and constituent balance closure
Development issues (local growth, SLC metropolitan area demands)
Policy Issues (3 states)
Agricultural issues (water supply, environmental compliance)
Environmental Issues (water quality, watershed management practices)
Ecological issues (Stream ecosystems, Bird refuge, GSL ecosystem)

## Slide 6: A common playground
The Great Salt Lake Basin Critical Zone Observatory
(Proposal submitted to NSF)

## Slide 7: Overarching Questions
How do climate variability and human induced landscape changes influence hydrologic processes, water quality and availability and the functioning of ecosystems to determine the flux of water and chemicals in rivers, lakes and aquifers?
What are the resource, social and economic consequences of these changes?
The Great Salt Lake provides the opportunity for closure of mass and water balances in a unique way useful to address these questions
Notes: These drive the compelling science

## Slide 8: Great Salt Lake Levels
The lake was divided into North and South arms by a railroad causeway in 1959. Separate records of level in the North Arm and South Arm are available from 1966.
(USGS data)
Feet
Meters
SLC Airport level
5/12/07 4197.4 ft 1279.4 m

## Slide 9: Level-Area-Volume Relationships
(Loving et al., 2000)
Volume (km3)
Area (km2)
Volume (km3)
Level (meter)
Level (meter)
Area (km2)

## Slide 10: Great Salt Lake Volumes
GSL was at its lowest water-surface elevation in recent history at about 1,277.4 m (4,191 ft), it covered about 2,460.5 km2 (950 mi2) and was about 7.6 m deep at its deepest point in 1963.
1987, when Great Salt Lake was at its highest water-surface elevation at about 1,283.8 m (4,212 ft) on April 1st, 1987, it covered about 6,216 km2 (2,400 mi2) and was about 13.7 m at its deepest point.
Acre-Feet  107
km3

## Slide 11: Conceptual Model
Air Humidity
Streamflow
Soil Moisture And Groundwater
Mountain Snowpack
Precipitation
Air Temp.
Evaporation
Solar Radiation
Salinity
GSL Level Volume Area
Processes that drive the GSL Volume fluctuations

## Slide 12
V (+ or -) m3
June 15 - Nov 1
Nov 1 - June 15
Volume Increase & Decrease each Year

## Slide 13
Streamflow gages
Corrine, Bear River
Drainage area 18,205 km2
Plain City, Weber River
Drainage area 5,390 km2
SLC, Jordan/Provo River Drainage area 8,904 km2
Provo, Provo River Drainage area 1,743 km2
Spanish, Jordan River Drainage area 1,689 km2

## Slide 14: Annual Streamflows
m3
USGS Data
1600 Mm3/year
520 Mm3/year
126 Mm3/year

## Slide 15: Nov 1 - June 15 lake volume increase
Annual total streamflow, Q (m3)
ΔV+ (m3) Nov 1 - June 15
1:1 line
Lake annual precipitation volume, P (m3)
LOWESS (R defaults)

## Slide 16: Great Salt Lake Evaporation from annual mass balance E = P+Q-V
Area m2
E m3
LOWESS (R defaults)

## Slide 17: Evaporation vs Temperature (Annual)
E/A m
Degrees C
LOWESS (R defaults)

## Slide 18: Annual Evaporation Loss E/A
Area m2
E/A m
Salinity decreases as volume increases. E increases as salinity decreases.
LOWESS (R defaults)

## Slide 19: Evaporation vs Salinity
E/A m
C = 3.5 x 1012 kg/(Volume) g/l
Salinity estimated from total load and volume related to decrease in E/A with decrease in lake volume and increase in C
LOWESS (R defaults)

## Slide 20: Volume decrease versus E (annual)
E m3
V- m3 June 15 -Nov 1
Significant E in excess of V-.
Evaporation not negligible when lake is rising (Nov 1 - June 15)
Streamflow input when lake is falling not negligible
1:1 line
(from annual mass balance E = P+Q-V)
LOWESS (R defaults)

## Slide 21: Evaporation...
Evaporation is the only outflow from the GSL,
Lake volume impacts salinity (dilution).
Evaporation from the GSL is sensitive to salinity which changes the saturation vapor pressure above the lake’s surface,
Salinity decreases as volume increases and visa versa.
RD2
(North Arm)
LVG4
(North Arm)
FB2
(South Arm)
AS2
(South Arm)
UGS Salinity Observation Sites

## Slide 22: Salinity & Evaporation within Overall System
Air Humidity
Streamflow
Soil Moisture And Groundwater
Mountain Snowpack
Precipitation
Air Temp.
Evaporation
Solar Radiation
Salinity
GSL Level Volume Area

## Slide 23: Lake Surface Salinity
Level (m)
TDS (g/l)
Pre 1986
Post 1987
North Arm
South Arm
LOWESS
West Desert Pumping Project
(Apr 1987 - Jun 1989)

## Slide 24: Total Salt Load Calculations
0.152 m
1.524 m
3.048 m
6.096 m
9.144 m
0.0m
3.810m
2.286m
0.762m
6.858m
bottom
Salinity recorded with multiple depths at one site
Notes: Flat line

## Slide 25
RD2
LVG4
Load = 3,620 M ton
Load = 3,200 M ton
Total Load
North Arm Load
South Arm Load

AS2
FB2
kg of TDS
South Arm
North Arm
Salt Load Dynamics, North, South, & Total Lake

## Slide 26: Constituents of the GSL
Date | TDS g/L | Level ft | Na % WT | K % WT | Mg % WT | Ca % WT | Cl % WT | SO4 % WT
1987, June 9th | 175.7 | 4210.7 | 32.2 | 3.3 | 1.9 | 0.2 | 56.5 | 5.9
1991, June 12th | 236.1 | 4201.0 | 33.5 | 2.9 | 1.7 | 0.2 | 55.7 | 6.0
1993, April 27th | 293.7 | 4197.4 | 32.5 | 3.3 | 2.1 | 0.1 | 55.7 | 6.3
1970, August 4th | 347.0 | 4194.8 | 31.4 | 3.9 | 3.0 | 0.1 | 53.4 | 8.2
1968, July 16th | 354.5 | 4194.4 | 25.6 | 4.2 | 2.7 | 0.1 | 56.4 | 11.0
Average |  |  | 31.0 | 3.5 | 2.3 | 0.1 | 55.5 | 7.5
Notes: Showing the constituents of the GSL on 5 dates spanning the range of salinity observed in the north arm from UGS data. The lowest total dissolved solids was 175.7 g/l on June 9th , 1987. The highest TDS was 354.5 g/l on July 16th ,1968. The dominant ions are Na, Cl which comprise 80 % of the ionic mass. Across the range of salinity observed the percentages of ionic mass contributed by each ion remain essentially constant. The high ionic strength observed in the GSL requires use of the Pizter equations to calculate the activity coefficient that is used to obtain vapor pressure. The USGS program PHreeqc was used to evaluate water activity coefficients. I am greatful to Lynn Dudley who helped me to learn how to use this and understand lake salinity and chemistry.

## Slide 27
Hydrogen Bond
Molecule
Water surface
Water Body
Air
Dissolved salts
Clouds
Ra
Rs
Latent Heat
Sensible Heat
Rl
Rns
Atmosphere
Salinity Impact on Evaporation
These molecules have sufficient energy to sever the bonds and enter the air α Ts
The rate of re-entering f (concentration)
αRs
Water activity coefficient

## Slide 28: Penman Equation modified for Salinity
Rn Net Radiation, λv latent heat of vaporization,
β water activity coefficient, νa wind speed
∆´ gradient of saturated vapor content of air corrected for salinity,
γ psychrometric constant, KE bulk latent-heat transfer coefficient.
Where:-

## Slide 29: The Activity of Water in Brines Using its Chemical Composition From USGS Model...
(Parkhurst and Appelo, 1999)

## Slide 30
Adjusted SVP (kpa)
Temperature (C)
Salinity Impact on GSL Saturation Vapor Pressure

## Slide 31
Penman Evaporation (m3)
Mass balance Evaporation (m3)
1:1 line

Un-modified Penman
modified Penman
LOWESS
(R-Defaults)
Evaluation of Modified Penman Equation

## Slide 32: Per Unit Area Comparison
Modified Penman Evaporation (meter)

## Slide 33: Possible Reasons for remaining Discrepancies
Errors in P, Q
Errors in ET Climate Data (T, Tdew, Wind Speed)
Errors in Lake Surface Properties
(Salinity, Roughness)
Errors in Effective Evaporating AreaErrors in Effective Area for Precipitation
Lake Heat Storage
Freshwater surface lenses

## Slide 34: Conclusions
Air Humidity
Streamflow
Soil Moisture And Groundwater
Mountain Snowpack
Precipitation
Air Temp.
Evaporation
Solar Radiation
Salinity
GSL Level Volume Area
Dominant
Reduces
(T,S)
Increases
Area Control
CL/V
Reduces
Contributes
Supplies

## Slide 35: Summary
Salinity decreases as Lake volume increases. Evaporation increases as salinity decreases. This is a stabilizing feedback.
Across the range of salinity observed the percentages of ionic mass contributed by each ion remain essentially constant.
The saturation vapor pressure over the GSL surface is reduced by (10% - 40%) due to salinity.
The Penman equation modified for salinity is closer to, but underestimates, mass balance evaporation estimates.