## Slide 1: Terrain Analysis for Water Quality Modeling
David G. Tarboton
Saurabh Gogate
Mariush Kemblowski
Qiang Shu
Eric Wahlstrom
Darwin L. Sorensen
David K. Stevens
http://www.engineering.usu.edu/dtarb
dtarb@cc.usu.edu

## Slide 2: Objectives
Incorporate GIS Methodology into the Source Water Protection and Pollution Assessment Process to provide information about potential contamination risks to drinking water supplies
Exploratory low data requirement assessment system for initial screening
Notes: Used by watershed managers to rank risks, and to prioritize protection activities

## Slide 3: Overview
The source water protection problem
Topographically driven screening model methodology
Representing the terrain flow field
TauDEM water quality functions

## Slide 4: The Need: Source Water Protection
Identify and Inventory potential sources of contamination
Visualize the locations of potential pollution sources and pathways that pollutants may follow
Exploratory modeling to assess pollution susceptibility for prioritization of analysis
Detailed analysis and risk assessment

## Slide 5: Assumptions for GIS Topography driven approach
Surface water and its associated contaminants move in directions following the topography.
Shallow subsurface flow follows topography and sustains baseflow.
Surface flows occur over a fraction of the time. Approximated as steady state.
Discharge separated into stormflow and baseflow assumed to represent surface and subsurface flow paths respectively.
Quantity of runoff generated from each grid cell proportional to annual rainfall.
Notes: The approach can provide screening level information without detailed modeling of infiltration, soils data etc.
Preferred over arbitrary setting of source water protection zones or buffers.

## Slide 6: Methodology
f = surface runoff time fraction
Stormflow/baseflow separation using HYSEP

## Slide 7: Runoff proportional to PRISM annual rainfall (inches)
Runoff coefficients
Steady state water inputs
Surface - average when active
Subsurface

## Slide 8: Topographically driven flow path assumption
?
Limitation imposed by 8 grid directions.

## Slide 9
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/dtarb/tarpubs.htm)

Proportion flowing to neighboring grid cell 1 is 2/(1 + 2)
Proportion flowing to neighboring grid cell 2 is 1/(1 + 2)
D Multiple flow direction model

## Slide 10
Contributing Area using D8
Contributing Area using D

## Slide 12: Inventory of potential contamination sources such as landuse designated industrial

## Slide 13: Conservative compound in surface runoff example
Surface runoff
Industrial area potential contamination source
Contaminant load
Contaminant concentration

## Slide 14
Surface runoff
Contaminant load
Contaminant concentration

## Slide 15
Useful for example to track where sediment or contaminant moves

## Slide 16
Useful for example to track where a contaminant may come from

## Slide 17
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 18
Useful for a tracking a contaminant released or partitioned to flow at a fixed threshold concentration

## Slide 19: Coupling to MODFLOW for subsurface simulation

## Slide 20: MODFLOW Boundary Conditions

## Slide 21: Nonpoint source nitrate loading based on landuse

## Slide 22: Nitrate concentration from MODFLOW+MT3D

## Slide 23: TauDEM Software Architecture
ESRI binary
grid
ASCII text
grid
ESRI grid API
(Spatial analyst)
gridio C++ library
shapelib C++ library
TauDEM C++ library
Fortran (legacy)
components
Standalone
command line
applications
C++ COM DLL interface
VB GUI
application
ESRI ArcGIS Toolbar
Vector shape
files
Data
formats
Available from
http://www.engineering.usu.edu/dtarb/
Binary direct
access grid

## Slide 24: TauDEM Software Functionality
Pit removal
Flow directions and slope
Drainage area (D8 and D)
Network and watershed delineation
Threshold/drainage density selection by stream drop analysis (Tarboton et al., 1991, Hyd. Proc. 5(1):81)
Water Quality Functions:
  Down slope Influence
  Upslope Dependence
  Concentration Limited Accumulation
  Transport limited accumulation
  Decaying Accumulation

## Slide 25: Conclusions
Take advantage of GIS Extendibility
Inventory and Integrate potential contaminant information from multiple sources
Exploratory screening model based upon simple assumptions facilitates visualization of potential pollution based upon readily available data for prioritization and further analysis