## Slide 1: Geographic Information System Based Hydrology in Ecology and Natural Resources Management
David G. Tarboton
dtarb@cc.usu.edu
http://www.engineering.usu.edu/dtarb

## Slide 2: Overview
Channel and watershed delineation
Hydrologic modeling (Bandaragoda)
Terrain stability mapping and erosion (Goodwin, Pack, Istanbulluoglu)
Dryland vegetation, a moisture limited ecological continuum (Goodwin)
Vegetation disturbance sediment model (Istanbulluoglu)

## Slide 3: Objective delineation of channel networks using digital elevation models
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in models.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.

## Slide 4: DEM based channel network delineation using local curvature and constant drop analysis to have objective and spatially variable drainage density
1
1
1
1
1
3
16
4
4
Accumulation of "valley" cells
4
5
6
3
7
2
1
8
Eight direction pour point model D8
Flow direction network
Local Valley Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58
Threshold = 10
Dd = 2.5 km-1
t = -3.5
Threshold = 20
Dd = 1.9 km-1
t = -1.03
Stream drop test for highest resolution network (smallest threshold) with constant drop property satisfied, i.e. t test indicates no statistically significant difference in mean drop between first order and all higher order streams.

## Slide 5
Curvature based stream delineation with threshold by constant drop analysis

## Slide 6
100 grid cell constant drainage area threshold stream delineation

## Slide 7
200 grid cell constant drainage area based stream delineation

## Slide 8: Model Element Spatial Resolution
Baron subwatersheds from streams delineated using objectively estimated drainage density from constant drop analysis.
Baron subwatersheds generalized based on third order streams.

## Slide 9: Topographic Slope
?
Topographic Definition Drop/Distance
Limitation imposed by 8 grid directions.
Flow Direction Field — if the elevation surface is differentiable (except perhaps for countable discontinuities) the horizontal component of the surface normal defines a flow direction field.

## Slide 10
The D Algorithm
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)

## Slide 11
Contributing Area using D8
Contributing Area using D

## Slide 12
Useful for example to track where sediment or contaminant moves

## Slide 13
Useful for example to track where a contaminant may come from

## Slide 14
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 15: Transport limited accumulation
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment

## Slide 16
Reverse Accumulation
Useful for destabilization sensitivity in landslide hazard assessment
with Bob Pack

## Slide 17: SINMAP
Terrain Stability Mapping
ArcView 3.x Extension
(Bob Pack, Craig Goodwin)

## Slide 18: TOPNET
Enhanced TOPMODEL (Beven and Kirkby, 1979 and later) applied to each subwatershed model element.
Kinematic wave routing of subwatershed inputs through stream channel network.
Vegetation based interception component.
Modified soil zone
Infiltration excess
GIS based parameterization
(TOPSETUP)
Snow (in progress)
Precipitation
Saturation Excess Runoff
Infiltration Excess Runoff
Baseflow
Soil Zone Drainage
zr
Soil Store
SR(m) =Soil Zone water content
Zr=depth of root zone
Throughfall
Streamflow
Precipitation
Soil moisture deficit/depth to water table from wetness index determines saturated area
Baseflow response from average soil moisture deficit
Saturated Zone State Variable
z
Reference ET demand
Priestly-Taylor
temp. and radiation based
Infiltration capacity
If z < zr SR is enhanced locally to
Local soil moisture enhancement
Interception Store
Canopy Capacity CC (m)
Canopy Storage CV (m)
With Christina Bandaragoda

## Slide 19
Basin 1
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.05
0.10
0.15
0.20
Basin 3
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 2
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
25
0.00
0.10
0.20
Basin 4
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
0.30
Basin 7
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 8
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 6
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 9
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.05
0.10
0.15
0.20
Wetness index histogram for each subwatershed used to parameterize subgrid variability of soil moisture
With Christina Bandaragoda

## Slide 20
Soil parameter look up by zone code
STATSGO Soil derived parameters
Soil texture for each of the 11 standard soil depth grid layers from PSU gridding of NRCS STATSGO data.
Table of Soil Hydraulic Properties – Clapp Hornberger 1978
Depth weighted average
Exponential decrease with depth
…
Soil Grid Layers
Joined to Polygon Layer
q1 ,, q2 , & yf
f & K
Zone Code Polygon Layer
With Christina Bandaragoda

## Slide 21: Basin average precipitation
Streamflow at outlet
Cumulative water balance

## Slide 22
“White space” is the Grey at Dobson minus Ahaura, Arnold and Grey at Waipuna

## Slide 23: Shear Stress Threshold Model for Channel Initiation
tf: Effective Shear Stress Overland Flow;
  Overland flow, qo;
    Contributing area, a
    Excess rainfall rate, r
  Roughness, n;
    Bare soil, or grains, nb(d50)
    Additional roughness, na
  Slope, S
tc :Critical Shear Stress
  -Sediment Size, d50
  -Dimensionless Critical Shear Stress, t*
Channels incise when;
tftc
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 24: The PCI Theory
Hydraulic and hydrologic hillslope properties are treated as random variables with spatially homogenous probability distributions.
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 25
Field observations
Channel head locations identified
Local slopes estimated in the field.
Contributing areas were derived from the DEM.
Sediment size samples were collected just above the headcuts.
Gully cross-section areas measured.
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 26
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 27: Point-wise Comparison of the Observed aSa and Calculated C at Channel Heads
The theory developed suggested that variation in d50, na and r is responsible for the variation in aS at channel heads. We used the measured values of d50 to test the contribution of d50 to this variability. We set =1.167, r = 35 mm/h, na= 0.052.
The regression R2 and Nash-Sutcliff (NS) error measure indicate that about 40% of the variability in observed aS may be attributed to d50.
R2=0.387
NS=0.377
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 28: Comparison of Channel Initiation Probability Distributions
Trapper Creek Data
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 29
PCI in Slope-Area Diagrams
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 30: Comparison of Channel Initiation Probability Distributions
Tennessee valley data set (Montgomery and Dietrich, 1989;1992).
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 31
PCI Maps of the Study Watersheds
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 32
Tr. 5
Tr. 15
Tr. 18
Tr. 19
Gully cross-sections are surveyed at
20-30 m spacing.
Slope of each segment is measured.
Sediment volumes are accumulated
downslope.
Field Estimates of Transport Capacity
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 33
Field Data;
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 34
as a function of
With Erkan Istanbulluoglu, Bob Pack, Charlie Luce

## Slide 35: Dryland Vegetation Distribution
Basic Premises
Moisture is the most significant resource limitation in drylands
Topography is a major factor regulating landscape moisture by:
  Redistribution of moisture by overland flow
    No subsurface lateral flow
  Solar radiation exposure
    South slope versus north slope
Craig Goodwin

## Slide 36
Topographic Factors
South-facing Hillslope
North-facing Hillslope
Solar Radiation Exposure
Moisture Redistribution
Craig Goodwin

## Slide 37: Ecological field data collection
Cover data collected at approximately 60 transects (30 m long) per watershed.
Cover data collected for 100 points per transect, by species, using the “point intercept on a transect method.”
Craig Goodwin

## Slide 38
Craig Goodwin

## Slide 39: Hydrology Component: Basis
Landscape moisture in drylands is derived from infiltration of precipitation (ip) and overland flow runon (iq).
Infiltration and runoff (q) are partitioned using a storage threshold (h) concept. Daily (storm) rainfalls (p) are derived from an exponential distribution. Total average annual runoff at a point (qa) is obtained by summing over the distribution of precipitation days. [Kirkby, 1994]
A fraction of runon (qin) infiltrates at a point. The fraction that infiltrates is a function of discharge and surface characteristics (ks), which control time of overland flow occurrence at that point.
Large bare ground expanses reduce soil moisture through evaporation. Currently, evaporation is estimated by a simple expression involving climate (kc) and solar radiation (R) parameters (kr), but more robust methods could be used.
A landscape moisture index (LMI), which is spatially distributed across a dryland landscape, is the end product of the hydrology component.
Craig Goodwin

## Slide 40: Landscape Moisture Index
Distribution of the landscape moisture index (LMI) across Kendall watershed. Transects average the LMI cell values of cells that they intersect, and are binned into four categories that match the LMI categories. The very dry sites are on the south facing slopes, whereas dry sites occur on north facing slopes. The damp and moist categories occur along the mainstem valley and the two major tributary valleys. Note how the LMI incorporates characteristics of solar radiation and overland flow discharge (and specific catchment area). In the table to the right, vegetation cover data are ordered by LMI and binned using the same categories as shown on the map above.
Cover and LMI data for 4 Species at 55 transects. Cover is number of species hits out of a possible 100.
Craig Goodwin

## Slide 41: Cover Frequency Chart
This graph illustrates the binned field data presented in the table on the previous slide. Only four of the 20 species in the watershed are illustrated. These data were used to predict species distribution across the landscape. Distribution of black gramma and velvet mesquite are illustrated on the next slide.
Craig Goodwin

## Slide 42: Species Distribution
Black gramma distribution based upon LMI.
Mesquite distribution based upon LMI.
Craig Goodwin

## Slide 43: Other Potential Indices: Do They Work As Well?
Craig Goodwin

## Slide 44
Vegetation Disturbance Sediment Model
Purposes
How do forest cover conditions influence the frequency and magnitude of stream sediment inputs.
How do natural and human disturbances alter these frequencies and magnitudes.
Motivated by biologic and aquatic community dependence on sediment input regime.
Erkan Istanbulluoglu

## Slide 45
MODELING APPROACH
Erkan Istanbulluoglu

## Slide 46
Recovery Following Wildfires
In the first few years following vegetation loss fluvial erosion is often observed during thunderstorms.
Following the initial significant increase erosion is suppressed by the growth of under-story vegetation and recovery of the infiltration rates (in 3 to 5 yrs)
Root-strength reduces to minimum values usually after 10 – 15 years and increases landslide susceptibility during this period.
Erkan Istanbulluoglu

## Slide 47
FOREST FIRES
Sampled Annual Maximum Rainfall
Runoff Response
Vegetation Response
Erosive Response
10000 years simulation
Erkan Istanbulluoglu

## Slide 48
CONSTANT ROOT COHESION (No Vegetation Disturbance)
Soil depth at a point
Summary of the simulations
Erkan Istanbulluoglu

## Slide 49
SASY (Observed)
LASY (Observed)
Event S.Y. (Observed)
95% Quantile
8% Quantile
Modeled Event S.Y.
Modeled LASY

## Slide 50: Conclusion
Spatial hydrologic processes play a key role in integrating hydrology with to other fields including Geomorphology, Ecology, and Environmental Policy and Management
Are there any questions ?
AREA 1
AREA 2
3
12
http://www.engineering.usu.edu/dtarb