## Slide 1: Managing Hydrologic Data, Observations and Terrain Analysis
http://www.engineering.usu.edu/dtarb/
David Tarboton
Utah State University

## Slide 2: Outline
The CUAHSI Hydrologic Information System
Terrain Analysis Using Digital Elevation Models
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/
http://hydrology.usu.edu/taudem

## Slide 3: Hydrologic Data Challenges
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
Data Heterogeneity

## Slide 4: The way that data is organized can enhance or inhibit the analysis that can be done
I have your information right here …
Picture from: http://initsspace.com/

## Slide 5: Hydrologic Science
Hydrologic conditions
(Fluxes, flows, concentrations)
Hydrologic Process Science
(Equations, simulation models, prediction)
Hydrologic Information Science
(Observations, data models, visualization
Hydrologic environment
(Physical earth)
Physical laws and principles
(Mass, momentum, energy, chemistry)
It is as important to represent hydrologic environments precisely with
data as it is to represent hydrologic processes with equations

## Slide 6: Data models capture the complexity of natural systems
NetCDF (Unidata) - A model for Continuous Space-Time data
Space, L
Time, T
Variables, V
D
Coordinate
dimensions
{X}
Variable dimensions
{Y}
ArcHydro – A model for Discrete Space-Time Data
Space, FeatureID
Time, TSDateTime
Variables, TSTypeID
TSValue
Terrain Flow Data Model used to enrich the information content of a digital elevation model
CUAHSI Observations Data Model: What are the basic attributes to be associated with each single data value and how can these best be organized?

## Slide 7: Data intensive science synthesizes large quantities of information (Hey et al., 2009).
exploiting advanced computational capability for the analysis and integration of large new datasets to elucidate complex and emergent behavior
In hydrology, the image at left (Ralph et al., 2006) illustrates connection between extreme floods recorded in USGS stream gages and atmospheric water vapor from space based sensors
Satellite remote sensing and massive datasets enhance understanding of multi-scale complexity in processes such as rainfall and river networks

## Slide 8: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 9: The CUAHSI Community Hydrologic Information System
University of Texas at Austin – David Maidment, Tim Whiteaker, James Seppi, Fernando Salas, Jingqi Dong, Harish Sangireddy
San Diego Supercomputer Center – Ilya Zaslavsky, David Valentine, Tom Whitenack, Matt Rodriguez
Utah State University – Jeff Horsburgh, Kim Schreuders, Stephanie Reeder, Edward Wai Tsui, Ravichand Vegiraju, Ketan Patil
University of South Carolina – Jon Goodall, Anthony Castronova
Idaho State University – Dan Ames, Ted Dunsford, Jiří Kadlec, Yang Cao, Dinesh Grover
Drexel University/CUNY – Michael Piasecki
WATERS Network – Testbed Data Managers
CUAHSI Program Office – Rick Hooper, Yoori Choi, Conrad Matiuk
ESRI – Dean Djokic, Zichuan Ye
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/

## Slide 10: What is CUAHSI?
Consortium of Universities for the Advancement of Hydrologic Science, Inc.
http://www.cuahsi.org/
110 US University members
6 affiliate members
12 International affiliate members
(as of March 2009)
Support
EAR 0753521
Infrastructure and services for the advancement of hydrologic science and education in the U.S.

## Slide 11
Data Searching – What we used to have to do
NWIS
NARR
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
Searching each data source separately
Michael Piasecki
Drexel University
Notes: 11

## Slide 12
What HIS enables
Searching all data sources collectively
NWIS
NAWQA
NARR
generic
request
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
ODM
Michael Piasecki
Drexel University
Notes: 12

## Slide 13: Video Demo
http://his.cuahsi.org/movies/JacobsWellSpring/JacobsWellSpring.html

## Slide 14: Web Paradigm
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search

## Slide 15: CUAHSI Hydrologic Information System Services-Oriented Architecture
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
ODM
Geo Data
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards
Information Model and Community Support Infrastructure

## Slide 16: What are the basic attributes to be associated with each single data value and how can these best be organized?
Value
DateTime
Variable
Location
Units
Interval (support)
Accuracy
Offset
OffsetType/ Reference Point
Source/Organization
Censoring
Data Qualifying Comments
Method
Quality Control Level
Sample Medium
Value Type
Data Type

## Slide 17: CUAHSI Observations Data Model
Streamflow
Flux tower
data
Precipitation
& Climate
Groundwater
levels
Water Quality
Soil
moisture
data
A relational database at the single observation level (atomic model)
Stores observation data made at points
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Standard format for data sharing
Cross dimension retrieval and analysis
Space, S
Time, T
Variables, V
s
t
Vi
vi (s,t)
“Where”
“What”
“When”
A data value

## Slide 18
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment and I. Zaslavsky, (2008), A Relational Model for Environmental and Water Resources Data, Water Resour. Res., 44: W05406, doi:10.1029/2007WR006392.
CUAHSI Observations Data Model http://his.cuahsi.org/odmdatabases.html
Notes: In designing ODM we asked: What are the basic attributes to be associated with each single data value and how can these best be organized? This involved community survey at a workshop and by email and based on the feedback received we came up with the ODM schema illustrated, published last year in WRR
This is quite a detailed slide, but it is the entire schema. Few database designs are simple enough to fit the entire schema on one slide. This shows at the center the data values table and off to the sides, the ancillary or metadata tables that record.

## Slide 19: Stage and Streamflow Example
Notes: Discharge Derived from Gage Height
Concepts:
Data derived from other data – single data point derived from a single observation (discharge from stage)
Data derived using a specific method (discharge from stage using rating curve)
Relationships:
Relationships between Values table and DerivedFrom table on DerivedFromID and ValueID
Relationship between Values table and Variables table on VariableID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID

## Slide 20
Feature
Waterbody
HydroID
HydroCode
FType
Name
AreaSqKm
JunctionID
HydroPoint
HydroID
HydroCode
FType
Name
JunctionID
Watershed
HydroID
HydroCode
DrainID
AreaSqKm
JunctionID
NextDownID
ComplexEdgeFeature
EdgeType
Flowline
Shoreline
HydroEdge
HydroID
HydroCode
ReachCode
Name
LengthKm
LengthDown
FlowDir
FType
EdgeType
Enabled
SimpleJunctionFeature
1
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
*
1
*
HydroNetwork
*
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
1
1
CouplingTable
SiteID
HydroID
Sites
SiteID
SiteCode
SiteName
Latitude
Longitude
…
Observations Data Model
1
1
OR
Independent of, but can be coupled to Geographic Representation
ODM
e.g. Arc Hydro

## Slide 21: Importance of the Observations Data Model
Provides a common persistence model for observations data
Syntactic heterogeneity (File types and formats)
Semantic heterogeneity
  Language for observation attributes (structural)
  Language to encode observation attribute values (contextual)
Publishing and sharing research data
Metadata to facilitate unambiguous interpretation
Enhance analysis capability

## Slide 22
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
GetSites
WaterOneFlow
Web Service
GetValues
GetSiteInfo
GetVariableInfo
Notes: 22

## Slide 23: WaterML as a Web Language
Discharge of the San Marcos River at Luling, TX June 28 - July 18, 2002
USGS Streamflow data in WaterML language
This is the WaterML GetValues response from NWIS Daily Values

## Slide 24: Open Geospatial Consortium Web Service Standards
Map Services
Web Map Service (WMS)
Web Feature Service (WFS)
Web Coverage Service (WCS)
Catalog Services for the Web (CS/W)
Observation Services
Observations and Measurements Model
Sensor Web Enablement (SWE)
Sensor Observation Service (SOS)
These standards have been developed over the past 10 years ….
…. by 400 companies and agencies working within the OGC
OGC Hydrology Domain Working Group evolving WaterML into an International Standard
http://www.opengeospatial.org/projects/groups/waterml2.0swg

## Slide 25: HydroServer – Data Publication
Ongoing Data Collection
Data presentation, visualization, and analysis through Internet enabled applications
Internet Applications
Point Observations Data
Historical Data Files
GIS Data
ODM Database
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
OGC Spatial Data Service from ArcGIS Server
Notes: A platform for publishing space-time hydrologic datasets that:
  Autonomous with local control of data
  Part of a distributed system that makes data universally available
Basis for Experimental Watershed or Observatory data management system
Standards based approach to data publication
  Accepted and emerging standards for data storage and transfer (OGC, WaterML)
Built on established software
  MS SQL Server, ArcGIS server
Open Source Community Code Repository
  Sustainability

## Slide 26: HydroServer
Manager Interface
Browser Interface
Service Interface
Map
Website
Time Series Analyst Website
HydroServer Website
Capabilities Web Service
HydroServer Capabilities Database
Capabilities Configuration Tool
Observation
Data Model
Observation
Data Model
WaterOneFlow Web Service
WaterOneFlow Web Service
WaterOneFlow Web Service
Observation
Data Model
Spatial Data Services
Geo Spatial
Database
Spatial Data File
HydroServer
View server portal
Publish point data
Publish spatial data
View spatial data
View point data
Configure server
Publish metadata
Load and Edit data
ODM Tools and Data Loaders

## Slide 27
HydroCatalog
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
Discovery and Access
Hydro
Desktop
Water Metadata Catalog
Harvester
Service Registry
Hydrotagger
Search Services
http://hiscentral.cuahsi.org
Search over data services from multiple sources
Supports concept based data discovery
CUAHSI Data Server
3rd Party Server
e.g. USGS

## Slide 28: HydroCatalog
Data Publisher Interface
Data Service Interface
Search Client Interface
Web Service Registry Website
Metadata Harvester
Metadata catalog database
Search Web Service
HydroCatalog
Validation Services
Monitoring Services
Semantic Annotation
Website
Logging Service
Validate WaterOneFlow Services
Collect Metadata
Register, View and Manage Services
View and Manage Ontology Mappings
Provide Client Search over Services and Observation Metadata
Log service use
Get Concepts and Mappings
Monitor Service
Hydrologic Ontology
Interactively test WaterOneflow Services
Ontology Web Service

## Slide 29: Overcoming Semantic Heterogeneity
ODM Controlled Vocabulary System
  ODM CV central database
  Online submission and editing of CV terms
  Web services for broadcasting CVs
Variable Name
Investigator 1: | “Temperature, water”
Investigator 2: | “Water Temperature”
Investigator 3: | “Temperature”
Investigator 4: | “Temp.”
ODM VariableNameCV
Term
…
Sunshine duration
Temperature
Turbidity
…
From Jeff Horsburgh

## Slide 30
Dynamic controlled vocabulary moderation system
Local ODM
Database
Master ODM Controlled Vocabulary
ODM Website
ODM Controlled
Vocabulary Moderator
ODM Data Manager
ODM
Controlled Vocabulary
Web Services
ODM
Tools
Local
Server
XML
http://his.cuahsi.org/mastercvreg.html
From Jeff Horsburgh

## Slide 31: Thematic keyword search
Integration from multiple sources
Search on space and time domain
HydroDesktop – Data Access and Analysis

## Slide 32: HydroDesktop
User
Interface
HydroDesktop
Core & Shared Libraries
Table View
Graph View
HydroR
Hydro Modeler
Help
Plugins
Application Settings
XML
Export to CSV
Fetch Basemap
DotSpatial
Library
WaterOneFlow
Web Service
WaterML
1.0
1.1
HydroCatalog
Search & Ontology Web Service
XML
Search
Project File
Project File
Project File
Metadata Cache DB
Metadata Cache DB
Metadata Cache DB
Data Repository DB
Data Repository DB
Data Repository DB
Object Model
Site
Variable
Series
Method
Theme
DataValue
…
Database Abstraction Layer
Data Repository Manager
Metadata Cache Manager
Search
Interact with user
Interact with user
Interact with other programs
Get from/ save to disk
Other
Libraries

## Slide 33: HydroModeler
An integrated modeling environment based on the Open Modeling Interface (OpenMI) standard and embedded within HydroDesktop
Allows for the linking of data and models as “plug-and-play” components
In development at the University of South Carolina by Jon Goodall, Tony Castronova, Mehmet Ercan, Mostafa Elag, and Shirani Fuller

## Slide 34
Integration with “R” Statistics Package

## Slide 35: 37 Water Data Services on HIS Central from 12 Universities
Dry Creek Experimental Watershed (DCEW) (28 km2 semi-arid steep topography, Boise Front)
68 Sites
24 Variables
4,700,000+ values
Published by Jim McNamara, Boise State University
University of Maryland, Baltimore County
Montana State University
University of Texas at Austin
University of Iowa
Utah State University
University of Florida
University of New Mexico
University of Idaho
Boise State University
University of Texas at Arlington
University of California, San Diego
Idaho State University

## Slide 36: Water Agencies and Industry
USGS, NCDC , Corps of Engineers publishing data using HIS WaterML
OGC Hydrology Domain Working Group evaluating WaterML as OGC standard
ESRI using CUAHSI model in ArcGIS.com GIS data collaboration portal
Kisters WISKI support for WaterML data publication
Australian Water Resources Information System Water Accounting System has adopted aspects of HIS
NWS West Gulf River Forecast Center Multi-sensor Precipitation Estimate published from ODM using WaterML

## Slide 37: CUAHSI Water Data Services Catalog
69 public services
18,000 variables
1.9 million sites
23 million series
5.1 billion data values
(as of June 2011)
The largest water data catalog in the world
maintained at the San Diego Supercomputer Center

## Slide 38: Open Development Model
http://hydrodesktop.codeplex.com
http://hydroserver.codeplex.com
http://hydrocatalog.codeplex.com

## Slide 39: Summary
Data Storage in an Observations Data Model (ODM) and publication through HydroServer
Data Access through internet-based Water Data Services using a consistent data language, called WaterML from HydroDesktop
Data Discovery through a National Water Metadata Catalog and thematic keyword search system at Central HydroCatalog (SDSC)
Integrated Modeling and Analysis within HydroDesktop
The combination of these capabilities creates a common window on water observations data for the United States unlike any that has existed before.

## Slide 40: Terrain Analysis Using Digital Elevation Models (TauDEM)
David Tarboton1, Dan Watson2, Rob Wallace,3 Kim Schreuders1, Jeremy Neff1
1Utah Water Research Laboratory, Utah State University, Logan, Utah
2Computer Science, Utah State University, Logan, Utah
3US Army Engineer Research and Development Center, Information Technology Lab, Vicksburg, Mississippi
This research was funded by the US Army Research and Development Center under contract number W9124Z-08-P-0420

## Slide 41: Deriving hydrologically useful information from Digital Elevation Models
Raw DEM
Pit Removal (Filling)
Flow Field
Flow Related Terrain Information
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 42: A parallel version of the TauDEM Software Tools
Improved runtime efficiency
Capability to run larger problems
Platform independence of core functionality
Deployed as an ArcGIS Toolbox with tools that drive accompanying command line executables, available from http://hydrology.usu.edu/taudem/

## Slide 43: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 44: Website and Demo
http://hydrology.usu.edu/taudem

## Slide 45: Grid Data Format Assumptions
Input and output grids are uncompressed GeoTIFF
Maximum size 4 GB
GDAL Nodata tag preferred (if not present, a missing value is assumed)
Grids are square (x= y)
Grids have identical extents, cell size and spatial reference
Spatial reference information is not used (no projection on the fly)

## Slide 46: Representation of Flow Field
D
D8
67
56
52
48
Steepest single direction
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 47: Parallel Approach
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 48: Illustrative Use Case: Delineation of channels and watersheds using a constant support area threshold
Steps
Pit Remove
D8 Flow Directions
D8 Contributing Area
Stream Definition by Threshold
Stream Reach and Watershed

## Slide 49: Pit Remove

## Slide 50: D8 Flow Direction (and Slope)

## Slide 51: D8 Contributing Area

## Slide 52: Stream Definition by Threshold

## Slide 53: Stream Reach and Watershed

## Slide 54: Some Algorithm Details Pit Removal: Planchon Fill Algorithm
Initialization
1st Pass
2nd Pass
Planchon, O., and F. Darboux (2001), A fast, simple and versatile algorithm to fill the depressions of digital elevation models, Catena(46), 159-176.

## Slide 55: Parallel Scheme
Communicate
Initialize( Z,F) Do for all grid cells i if Z(i) > n F(i) ← Z(i) Else F(i) ← n i on stack for next pass endfor Send( topRow, rank-1 ) Send( bottomRow, rank+1 ) Recv( rowBelow, rank+1 ) Recv( rowAbove, rank-1 ) Until F is not modified
Z denotes the original elevation.
F denotes the pit filled elevation.
n denotes lowest neighboring elevation
i denotes the cell being evaluated
Iterate only over stack of changeable cells

## Slide 56: Parallelization of Contributing Area/Flow Algebra
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-2
Queue’s empty so exchange border info.
B=-1
A=1
A=1
A=1
D=0
A=3
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-2
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
D=0
D=0
A=1
D=1
D=1
resulting in new D=0 cells on queue
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
A=5.5
A=2.5
A=1
A=6
A=3.5
and so on until completion
A=1
A=1
A=1
D=0
D=0
D=0
A=1
D=2
D=1
A=1
D=1
D=1
D=0
D=0
D=0
D=1
D=3
D=1
D=0
D=2
D=1
D=0
D=3
D=1
A=1
D=0
D=0
D=1
D=2
D=0
A=1
D=2
D=1
D=0
D=2
D=1
A=1
A=1
D=0
D=1
D=1
D=0
A=1
D=2
D=1
A=1
D=1
D=1
A=1
A=1
A=1
D=1
D=0
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-1
Decrease cross partition dependency
Executed by every process with grid flow field P, grid dependencies D initialized to 0 and an empty queue Q. FindDependencies(P,Q,D) for all i for all k neighbors of i if Pki>0 D(i)=D(i)+1 if D(i)=0 add i to Q next
Executed by every process with D and Q initialized from FindDependencies. FlowAlgebra(P,Q,D,,) while Q isn’t empty get i from Q i = FA(i, Pki, k, k) for each downslope neighbor n of i if Pin>0 D(n)=D(n)-1 if D(n)=0 add n to Q next n end while swap process buffers and repeat
1. Dependency grid
2. Flow algebra function

## Slide 57: Illustration of some other functions
D-Infinity Slope and Contributing Area

## Slide 58: Transport limited accumulation
Supply
Capacity
Transport
Deposition
2
2
)
tan(
b
T
cap
ca
=
å
+
=
}
,
min{
cap
in
out
T
T
S
T
å
-
+
=
out
in
T
T
S
D
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment
S

## Slide 59
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 60: Capabilities Summary
Capability to run larger problems |  |  |  | 
 |  | Processors used | Grid size | 
 |  |  | Theoretcal limit | Largest run
2008 | TauDEM 4 | 1 | 0.22 GB | 0.22 GB
Sept 2009 | Partial implement-ation | 8 | 4 GB | 1.6 GB
June 2010 | TauDEM 5 | 8 | 4 GB | 4 GB
Sept 2010 | Multifile on 48 GB RAM PC | 4 | Hardware limits | 6 GB
Sept 2010 | Multifile on cluster with 128 GB RAM | 128 | Hardware limits | 11 GB
1.6 GB
0.22 GB
4 GB
6 GB
11 GB
At 10 m grid cell size
Single file size limit 4GB

## Slide 61: Improved runtime efficiency
Parallel Pit Remove timing for NEDB test dataset (14849 x 27174 cells  1.6 GB).
128 processor cluster
16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
8 processor PC
Dual quad-core Xeon E5405 2.0GHz PC with 16GB RAM

## Slide 62: Improved runtime efficiency
Parallel D-Infinity Contributing Area Timing for Boise River dataset (24856 x 24000 cells ~ 2.4 GB)
128 processor cluster
16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
8 processor PC
Dual quad-core Xeon E5405 2.0GHz PC with 16GB RAM

## Slide 63: Scaling of run times to large grids
Dataset | Size | Hardware | Number of Processors | PitRemove (run time seconds) |  | D8FlowDir (run time seconds) | 
 | (GB) |  |  | Compute | Total | Compute | Total
GSL100 | 0.12 | Owl (PC) | 8 | 10 | 12 | 356 | 358
GSL100 | 0.12 | Rex (Cluster) | 8 | 28 | 360 | 1075 | 1323
GSL100 | 0.12 | Rex (Cluster) | 64 | 10 | 256 | 198 | 430
GSL100 | 0.12 | Mac | 8 | 20 | 20 | 803 | 806
YellowStone | 2.14 | Owl (PC) | 8 | 529 | 681 | 4363 | 4571
YellowStone | 2.14 | Rex (Cluster) | 64 | 140 | 3759 | 2855 | 11385
Boise River | 4 | Owl (PC) | 8 | 4818 | 6225 | 10558 | 11599
Boise River | 4 | Virtual (PC) | 4 | 1502 | 2120 | 10658 | 11191
Bear/Jordan/Weber | 6 | Virtual (PC) | 4 | 4780 | 5695 | 36569 | 37098
Chesapeake | 11.3 | Rex (Cluster) | 64 | 702 | 24045 |  | 
Owl is an 8 core PC (Dual quad-core Xeon E5405 2.0GHz) with 16GB RAM
Rex is a 128 core cluster of 16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
Virtual is a virtual PC resourced with 48 GB RAM and 4 Intel Xeon E5450 3 GHz processors
Mac is an 8 core (Dual quad-core Intel Xeon E5620 2.26 GHz) with 16GB RAM

## Slide 64: Scaling of run times to large grids
Chart: PitRemove run times
| 0.12000000000000002 | 2.14 | 4
Compute (OWL 8) | 9.5315 | 529.3877 | 4817.6293
Total (OWL 8) | 12.0132 | 680.5546 | 6224.5029
Compute (VPC 4) | 1502.2881 | 4779.8761
Total (VPC 4) | 2120.0307 | 5695.2647
Compute (Rex 64) | 10.3477 | 139.9145 | 701.7363
Total (Rex 64) | 255.8499 | 3758.8385 | 24045.0594
Owl is an 8 core PC (Dual quad-core Xeon E5405 2.0GHz) with 16GB RAM
Rex is a 128 core cluster of 16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
Virtual is a virtual PC resourced with 48 GB RAM and 4 Intel Xeon E5450 3 GHz processors
Chart: D8FlowDir run times
| 0.12000000000000002 | 2.14 | 4
Compute (OWL 8) | 355.6897 | 4363.094 | 10558.4924
Total (OWL 8) | 357.8926 | 4570.5555 | 11599.0188
Compute (VPC 4) | 10658.033 | 36568.8896
Total (VPC 4) | 11191.1583 | 37098.2448
Compute (Rex 64) | 198.0345 | 2854.9228
Total (Rex 64) | 429.8418 | 11384.6786

## Slide 65: Summary and Conclusions
Parallelization speeds up processing and partitioned processing reduces size limitations
Parallel logic developed for general recursive flow accumulation methodology (flow algebra)
Documented ArcGIS Toolbox Graphical User Interface
32 and 64 bit versions (but 32 bit version limited by inherent 32 bit operating system memory limitations)
PC, Mac and Linux/Unix capability
Capability to process large grids efficiently increased from 0.22 GB upper limit pre-project to where < 4GB grids can be processed in the ArcGIS Toolbox version on a PC within a day and up to 11 GB has been processed on a distributed cluster (a 50 fold size increase)

## Slide 66: Limitations and Dependencies
Uses MPICH2 library from Argonne National Laboratory http://www.mcs.anl.gov/research/projects/mpich2/
TIFF (GeoTIFF) 4 GB file size (for single file version)
Capability to use multiple files to cover domain not yet on web site
Processor memory
Toolbox user interface only for ArcGIS 9.3.1

## Slide 67: Are there any questions ?
AREA 1
AREA 2
3
12