## Slide 1: The WATERS Network: Design Strategy
WATERS Community Workshop
March 24-25, 2008
David Tarboton
Utah State University
Design Team
Barbara Minsker (PI), Roger Bales, John Braden, Susan Brantley, Martha Conklin, Elizabeth Eschenbach, Jeffrey Glass, Charles Haas, Thomas Harmon, Richard Hooper, James Myers, Chris Paola, Jerald Schnoor, David Tarboton
Notes: 1

## Slide 2
The questions that we ask as scientists shape everything that follows
How do hydrologic and related Earth surface systems respond to natural and human induced changes in climate and the environment?
How do multi-scale natural, managed and engineered processes and systems affect the water environment, and how can those processes and systems be modeled, designed, and optimized for sustainability?
How do people understand water processes and organize themselves, individually and collectively at different scales, to respond to challenges in the water environment?
Precisely relate the measurements being proposed to the questions being addressed
Notes: 2
These are our broad and overarching questions. Some say that they are too broad and there is discussion on focusing them more narrowly. These questions do address the basic knowledge needed to understand, engineer, manage, and set policy for water resources systems and infrastructure that are critical for life and society. These questions embody deep puzzles at the heart of Earth science, involving the role played by the water cycle in Earth systems, and they recognize that human choices and engineering play an important role in the functioning of the Earth’s water environment.
The design strategy is guided by the need to precisely relate the measurements being proposed to the questions being addressed.

## Slide 3: Outline
Research requirements
  Five example science requirement white papers
  Common observation requirements
Data Products
Spatial Stratification
Network infrastructure
  Measurement requirements and capabilities
  Observatory configuration and facilities
  Cyberinfrastructure
  Centralized facilities

## Slide 4: Five Example Research Questions
Hydrology and Runoff Generation
Sediment, Erosion and Geomorphology
Source water variability and dynamic treatment control
Soils and the Critical Zone
Human actions, Integration, Sustainability and resiliency, socio-economics
Notes: The SEDS document approached the design through a series of 5 example case studies that are presented as white papers in the appendix, and summarized briefly in chapter 4. These were chosen only as examples, not to be comprehensive, and were also selected based on the expertise and interests of the design team. These questions cover a diverse set of topics of interest to the communities involved in planning the WATERS Network.
The first question focuses on streamflow generation mechanisms, that is, the combination of surface and subsurface processes, both physical and biological, that control the movement of water through the landscape and result in streamflow, an observable property. This topic is further elaborated on from a geological and biogeochemical perspective in question two by examining the controls on the subsurface boundary layer of the critical zone, which is the zone of active exchange with surface processes. The third question examines sediment generation and transport and involves the mechanisms of erosion and fluvial geomorphology. The fourth question examines how water treatment can be improved with improved knowledge and forecasting of influent water quality. Finally, the last question examines how all of the knowledge, data, and models generated to address the first four questions can be coupled with additional engineering and socio-economic research to explore novel approaches to adaptive and integrated water resource management, particularly focusing on large-scale integrated treatment and socio-economic strategies.

## Slide 5: The domain of interest is the water environment where water plays an active role in shaping the earth and the environment (natural and human) functions to partition water inputs
Image from Anderson et al., 2004
Notes: The domain is the water environment. This critical zone from the top of vegetation down to the base of active groundwater where water plays an active role in shaping the earth and where the environment serves to partition water inputs.

## Slide 6: Observe the water environment functional behavior (partition, storage and release) through combinations of measurements to give as a product integral measures of water and water borne constituent fluxes and stores
Wagener, T., M. Sivapalan, P. Troch and R. Woods, (2007), "Catchment Classification and Hydrologic Similarity," Geography Compass, 1(4): 901, doi: 10.1111/j.1749-8198.2007.00039.x.
Notes: The strategy is to observe the water environment functional behavior (partition, storage and release) through combinations of measurements to give as a product integral measures of water and water borne constituent fluxes and stores. The key concept in the design, and in the justification for WATERS is that observations of single processes have reached a point of diminishing returns and that to really address the questions about response to change, scale dependence and human interactions that we need to combine information from multiple lines of evidence to develop integrated data products that can be used to get at understanding functional behavior.

## Slide 7: How do streamflow generation mechanisms vary with climate, land cover, topography and geology?
Evapotranspiration fraction
Dryness (available energy /precip)
1
humid
arid
energy limited
water limited
R/P
E/P
E = R : energy limited upper bound
large
small
Retention or Residence time
medium
E = P : water limited upper bound
Theoretical functional form
f(R/P, W/(P))
Notes: I will touch on each example question briefly, but refer you to the white papers in the appendix for details.
For each question we examined:
Scientific importance
Barriers and enabling technology
Example derivative questions and approaches to address them
Design at the network level
Design at the observatory level
Expected outcomes
The streamflow generation question is building on the partitioning ideas of Budyko and others, initially advanced in climatology. I think that these ideas provide the basis for a unified approach to testing hypotheses in WATERS.

## Slide 8
1
humid
arid
energy limited
water limited
R/P
E/P
Evaporative fraction
Dryness (available energy /precip)
E = R : energy limited upper bound
large
small
Retention or Residence time
medium
E = P : water limited upper bound
Preferential infiltration, Weiler
Threshold runoff – Woods et al., 2001
How does this …
Depend
on these …

## Slide 9: What is the depth and time scale of “active” fluid, energy, and nutrient circulation at the earth’s surface and what environmentally important variables control the evolution of this flow zone?
Cross section imaged by ground penetrating radar (GPR) (Lin, 2006).

## Slide 10: What are the sources, fluxes, and sinks of sediment in natural and human-modified landscapes; how are they distributed in space and time; and what controls production, transfer and storage rates?
Concave morphology causes rill erosion, convex causes sheet erosion

## Slide 11: How can adverse environmental impacts of source water variability best be reduced through dynamically controlled water treatment practices linked to real-time sensor systems with continuous computer modeling and adaptive sampling capabilities?
Power spectrum of contaminant occurrences in typical urban surface waters. From Beck (2005).
1
10
100
1000
0
200
400
600
800
1000
1200
1400
Time
Concentration
influent
usual effluent
desired

## Slide 12: To what extent can real-time sensors enable integrated and adaptive water management of stormwater, wastewater, and water supply, thereby improving sustainability and resiliency? How is the resiliency and long-term sustainability of such a system affected by choices among centralized and centralized treatment technologies?

## Slide 13: Common Observation Requirements
Stores of water and water borne constituents
  Surface water (lakes, rivers, snow, infrastructure, biota)
  Soil moisture
  Ground water
Fluxes of water and water borne constituents
  Precipitation, Evapotranspiration, Energy
  Streamflow, subsurface flow, constituent concentrations
Rates for biological, chemical and geomorphological processes
Residence times
Notes: In examining these questions we find that a common set of core data needs emerges that are required and have the potential to transform water research across these diverse areas. These are listed here and should form the basis for the WATERS Network data products.

## Slide 14: Outline
Research requirements
  Five example science requirement white papers
  Common observation requirements
Data Products
Spatial Stratification
Network infrastructure
  Measurement requirements and capabilities
  Observatory configuration and facilities
  Cyberinfrastructure
  Centralized facilities

## Slide 15: An integrated product giving the state of the water environment across the continent
?
Notes: So how might we take advantage of the MREFC opportunity, a capital equipment fund to, to fulfill these data needs. I suggest that we need to focus on an integrated data product that can give the state of the water environment across the continent. This slide shows the continental US subdivided into the USGS HUC 8 subbasins. There are 2117 of them with an average area of 4000 km2. This is the scale of relevance to many practical problems, the scale for which the functional behavior of the water environment is an important unsolved problem.
Are there examples we can learn from?

## Slide 16: EarthScope US Array
From David Simpson, IRIS
Notes: This slide with material from David Simpson shows the EarthScope US Array of siesmic stations. Earthscope is held up as a poster child MREFC project. It uses advanced technology to get at the variables of interest and provides a community data product that probes the deep structure and geologic and tectonic processes involved in the formation of the continent and the processes controlling earthquakes and volcanic eruptions.

## Slide 17: US Array Animation
If technically feasible show animation from
http://eqseis.geosc.psu.edu/~cammon/QA/sumatra12Sep2007.html
Instructions at
http://eqseis.geosc.psu.edu/~cammon/QA/

## Slide 18
http://water.usgs.gov/waterwatch/
Notes: In the water area this slide shows the USGS Waterwatch web page that gives streamflow across the nation. In fact from USGS stream gauges we already have a good network of streamflow.

## Slide 19: Integrated data product needs
Fluxes
  Precipitation and snow
  Evapotranspiration and sublimation
  Withdrawals, consumptive uses, return flows
Stores
  Surface water
  Soil moisture
  Groundwater
  Infrastructure (reservoirs)
Constituents
Notes: What is missing though is information about the inputs, precipitation and snowmelt, stores in reservoirs, the soil and groundwater, and constituents that comprise water quality, including sediments, nutrients, and many other pollutants. There is technology available to measure many of these and the WATERS Network proposes to install this technology in a national network to provide a comprehensive data product, that can be used to probe the water processes and water environment functional behavior to solve the open water environment grand challenge problems.

## Slide 20: Outline
Research requirements
  Five example science requirement white papers
  Common observation requirements
Data Products
Spatial Stratification
Network infrastructure
  Measurement requirements and capabilities
  Observatory configuration and facilities
  Cyberinfrastructure
  Centralized facilities

## Slide 21: Human Influenced Water Resource Classification (HIWRC)
Capture the diverse hydrologic conditions that exist across the US.
Set of variables that quantify hydrologic setting, both physical and human influenced
Variables mapped to ordinal scale
Principal Component and ISODATA Cluster Analysis
  Hutchinson and Schnoor – Appendix B
Notes: A common requirement at the network level is to site observatories in diverse settings representative of the natural and human influenced environment variability across the North American continent. Appendix B by Hutchinson and Schnoor describes an approach for stratification of the continent using statistical cluster analysis. This analysis resulted in a set of 12 human influenced water resources classes that span the diversity of settings that WATERS Network needs to consider.

## Slide 22: HIWRC Variables
Population Density (2000 Census)
Land Cover (NLCD, 2001)
Precipitation (PRISM)
Temperature (PRISM)
Soil Permeability (from STATSGO)
Slope (as derived from NED by PRISM)
Bedrock Permeability (from USGS lithologic group)
Water Use (USGS 2000 National Aggregate Water-Use Data System)

## Slide 23: HIWRC Variable Maps
Water Stress Index
Bedrock Permeability
Population Density
Land Cover

## Slide 24: PCA Component Loadings

## Slide 25: Twelve delineated HIWRCs

## Slide 26: Outline
Research requirements
  Five example science requirement white papers
  Common observation needs
Data Products
Spatial Stratification
Network infrastructure
  Measurement requirements and capabilities
  Observatory configuration and facilities
  Cyberinfrastructure
  Centralized facilities

## Slide 27: WATERS Network: Advancing Multi-Disciplinary Knowledge Through Integrated Infrastructure
Engineers
Geoscientists
Social Scientists
Others…
Notes: 27
This slide shows the WATERS Network components that are envisaged. These consist of observatories, experimental and field facilities, education and outreach facilities, informatics and cyberinfrastructure facilities, synthesis and modeling facilities and sensor and measurement facilities. Most of my time will be spent on the physical measurement facilities – because they are the hardest.

## Slide 28: Physical measurement requirements and capabilities
Measurement variables from example requirement papers (Table 5.1)
Water store and flux sensor systems (Table 5.2)
Waterborne constituent sensor systems (Table 5.3)
Notes: We have started a process of examining the measurements required to address the research questions and produce the data products and matching of these with capabilities. I am not going to go through these in detail. I will illustrate a few of the sensors and systems that are available to give you a sense for what is possible, and refer you to the tables in the SEDS document chapter 5 to read more.

## Slide 29: Physical Sensors
Parameter | Field-Readiness | Scalability | Cost
Temperature | High | High | 50–100
Moisture Content | High | High | 100–500
Flow rate, Flow velocity | High | Medium–High | 1,000–10,000
Pressure | High | High | 500–1,000
Light Transmission (Turbidity) | High | High | 800–2,000
From Tom Harmon

## Slide 30: Chemical Sensors
Parameter | Field-Readiness | Scalability | Cost ($)
Dissolved Oxygen | High | High | 800–2,000
Electrical Conductivity | High | High | 800–2,000
pH | High | High | 300–500
Oxidation Reduction Potential | Medium | High | 300–500
Major Ionic Species (Cl-, Na+) | Low–Medium | High | 500–800
Nutrients (Nitrate, Ammonium) | Low–Medium | Low–High | 500–25000
Heavy metals | Low | Low | NA
Small Organic Compounds | Low | Low | NA
Large Organic Compounds | Low | Low | NA
From Tom Harmon

## Slide 31: Embeddable Sensors: Current Status and Outlook
Physical Sensors…increasingly smaller, cheaper
Chemical Sensors: gross concentrations, changes
Acoustic and Image data samples
Acoustic, Image sensors with on board analysis
Chemical Sensors: trace concentrations, universal sensors (lab-on-a-chip)
DNA microarrays onboard embedded device, universal sensors
Sensor triggered sample collection (bridging technology)
present
future
Organism tagging, tracking
abiotic
biotic
DNA biosensors for targeted microorganism
From Tom Harmon

## Slide 32: Integrated Adaptive Soil Observation System
Feedback-Control system
Always looking several irrigation events ahead to prepare to adapt to condition changes
Y Park & T Harmon, CENS-Merced

## Slide 33
Multi-scale and Multi-Modal Sensing It is ready!
Drawing by Jason Fisher
UC Merced/WN/CENS-UCLA

## Slide 34
5th order Observatory
3rd order Cluster containing catchments draining directly to 1st, 2nd and 3rd order streams
1st order catchment
Terrestrial sensor package over catchment
Stream sensor package
Nested River Basin Observatory Design
Notes: We are considering two observatory configurations. The first is a nested river basin observatory design. This would deploy networks of sensors in catchments organized to represent a hierarchy of scales within a river network. The configuration suggested is:
Observatory: 5th order watershed 104 to 105 km2. 10 to 12 of these continent wide to span the HIWRC classes.
Three 3rd order clusters within each Observatory. 5 to 20 km2. Chosen to represent low, medium and high "Retention"
Four 1st order catchments within each cluster. 0.5 to 2 km2 Two first order, two draining directly to 2nd and 3rd order streams.

## Slide 35: Gradient Observatory Design
Systematic data collection across gradients to allow isolation of individual causative factors

## Slide 36: Catchment Instrumentation
Plot
Group
Flux tower and footprint
Streamgage
Subwatershed
Embedded soil moisture sensor network
Microgravity stations
ETRS (Flux) arrays
Fiber optic along stream for temperature
ADCP Streamflow
Isotope and chemical tracing

## Slide 37: Experimental Village
Decision
Theater
Dual Distribution System
Water
Use
Monitor
Grey Water
Recycling
System
Bioswale
Instrumented Sewer
Experimental
Treatment
Facility
Green Roof
Instrumented
Hillslope
Tree Filter
Porous Pavement

## Slide 38: Experimental Farm
Bioswale
Tree Filter
Instrumented Cornfield
Instrumented Experimental Hillslope
Membrane Bioreactor
Instrumented Stream

## Slide 39: Environmental Cyber Infrastructure Architecture: Research Services
Notes: 39

## Slide 41: Environmental CI Projects that Demonstrate Feasibility of WN Vision
CUAHSI Hydrologic Information System project
WN testbed projects
Cyberinfrastructure for Environmental Observatories: Prototype (CEO:P) projects
NCSA Environmental CI Demonstrator/TRECC project
Many others…

## Slide 42
CUAHSI Hydrologic Information System:
Service Oriented Architecture for Water Resources Data
WaterOneFlow Web Services
Data access through web services
Data storage through web services
Downloads
Uploads
Observatory data servers
CUAHSI HIS data servers
3rd party data servers
e.g. USGS, NCDC
GIS
Matlab
IDL
Splus, R
Excel
Programming (Fortran, C, VB)
Analysis and Modeling applications
Data Access System for Hydrology (DASH)
Website Portal and Map Viewer
Preliminary data exploration and discovery. See what is available and perform exploratory analyses
HTML -XML
WSDL - SOAP
ODM
ODM
Internet
WaterML
Notes: Hydrologic Information System Service Oriented Architecture

## Slide 43: HIS Implementation in WATERS Network Information System
11 WATERS Network test bed projects
16 ODM instances (some test beds have more than one ODM instance)
Data from 1246 sites, of these, 167 sites are operated by WATERS investigators
National Hydrologic Information Server
San Diego Supercomputer Center

## Slide 44: Virtual Observatories
Montagna stations
SERF stations
TCOON stations
USGS gages
TCEQ stations
Hypoxic Regions
NCDC station
e.g. Corpus Christi Bay
Dashboard summarizing current conditions in Corpus Christi Bay (left)
Virtual meeting at a bay in Second Life (right).

## Slide 45: Modeling, Visualization and Synthesis
Rain
Vegetation
Soil Type
Topography
Runoff
Model Output Evaluation
(Images from Ross Woods and Luis Bastidas)
Databases
Analysis
Models

## Slide 46: Fiber optic
Stream
http://www.cuahsi.org/cyberseminars/Selker-20070504.pdf
Sensor and Measurement Facilities
Electromagnetic induction (EMI) to determine soil properties

## Slide 47: Summary
Multi-scale observatory approach
  Remote sensing (air, satellite)
  Nested static sensors
  Mobile sensors
  Experimental facilities
Cyberinfrastructure
Central Facilities
Water Science and Engineering Research is at a point where there are diminishing returns from PI level projects and to achieve new breakthroughs, multidisciplinary study that integrates diverse measurements using advanced technology to examine processes at multiple scales is required