## Slide 1: Application of TopNet to DMIP
Christina J. Bandaragoda1
David G. Tarboton1
Ross Woods2
1. Utah State University, Civil & Environmental Engineering Department, Logan, UT
2. National Institute of Water and Atmospheric Research, NIWA, Christchurch, New Zealand

## Slide 2: TOPNET
Enhanced TOPMODEL (Beven and Kirkby, 1979 and later) applied to each subwatershed model element.
Kinematic wave routing of subwatershed inputs through stream channel network.
Vegetation based interception component.
Modified soil zone
Infiltration excess
GIS based parameterization
(TOPSETUP)
Snow (in progress)
Precipitation
Saturation Excess Runoff
Infiltration Excess Runoff
Baseflow
Soil Zone Drainage
zr
Soil Store
SR(m) =Soil Zone water content
Zr=depth of root zone
Throughfall
Streamflow
Precipitation
Soil moisture deficit/depth to water table from wetness index determines saturated area
Baseflow response from average soil moisture deficit
Saturated Zone State Variable
z
Reference ET demand
Priestly-Taylor
temp. and radiation based
Infiltration capacity
If z < zr SR is enhanced locally to
Local soil moisture enhancement
Interception Store
Canopy Capacity CC (m)
Canopy Storage CV (m)

## Slide 3: Spatial Representation
Subwatershed and channel reach model elements
Model is lumped at the scale of each subwatershed
Binary topological linkage with internal reaches split into two logical reaches with flow from reach watershed entering at midpoint
1
9
2
4
5
6
18
19
20
31
21
22
30
23
24
25
29
26
27
28
7
3
8
1
Subwatershed
18
Channel reach
Flow recorder
Logical Topology
Physical layout

## Slide 4: Some model details
Assumption 1.
Hydraulic conductivity decreasing with depth - sensitivity parameter f
Assumption 2.
Saturated lateral flow driven by topographic gradient and controlled by depth to water table (soil moisture deficit).
Assumption 3.
Steady state. Saturated lateral flow related to equilibrium recharge rate.
Determines depth to water table and
saturation excess runoff generation
when z < 0

## Slide 5: Additions and Modifications

## Slide 6: Potential Evapotranspiration (following Maidment D. R. (editor), 1993, Handbook of Hydrology, Chapter 4 on Evaporation by W J Shuttleworth.)
A = Available energy = (1-a)Tf So - f e’ s T4
f = Tf/a Cloudiness factor
D = gradient of saturated vapor pressure - temperature curve at air temperature
g = psychometric constant at air temperature and pressure
e’ = net emmissivity based upon dew point
ae = 0.34 be = -0.14 kPa-1/2
Temperature and dew point lapsed from measurements at measurement location
Notes: Could reduce PET for non growing season

## Slide 7: Interception (adapted following Ibbitt, 1971)
Throughfall f(CV)
Relative intercepted storage CV/CC
1
1

## Slide 8: Soil Zone
Green-Ampt like infiltration
excess rate formulation
Plant
Available
Drainable
Dq2
Dq1
zr
ET/PET
SOILC = zr (Dq1+ Dq2)
Soil Drainage
1
Drainage/Recharge r

## Slide 9: Inputs Forcing
Precipitation at each radar grid location. Subwatershed precipitation by Delauney triangle weighted averaging over each subwatershed.
Air Temperature, Dew Point at single location, adjusted to center of each subwatershed using lapse rate.

## Slide 10: Outputs
Streamflow for designated reaches
Diagnostic output for each subwatershed
  Total runoff
  Infiltration excess runoff component
  Saturation excess runoff component
  Baseflow component
  Drainage from soil to saturated zone (Recharge)
  Saturated area
  Potential evapotranspiration
  Actual evapotranspiration
Time series of model state variables
  Mean water table depth
  Soil zone storage
  Canopy storage

## Slide 11: Objective delineation of channel networks using digital elevation models
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and delineate model elements that account for this.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.

## Slide 12: DEM based channel network delineation using local curvature and constant drop analysis to have objective and spatially variable drainage density
1
1
1
1
1
3
16
4
4
Accumulation of "valley" cells
4
5
6
3
7
2
1
8
Eight direction pour point model D8
Flow direction network
Local Valley Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58
Threshold = 10
Dd = 2.5 km-1
t = -3.5
Threshold = 20
Dd = 1.9 km-1
t = -1.03
Stream drop test for highest resolution network (smallest threshold) with constant drop property satisfied, i.e. t test indicates no statistically significant difference in mean drop between first order and all higher order streams.

## Slide 13
Curvature based stream delineation with threshold by constant drop analysis

## Slide 14: Control of Spatial Resolution
Baron subwatersheds from streams delineated using objectively estimated drainage density from constant drop analysis.
Baron subwatersheds generalized based on third order streams. For results generated to date 3rd order generalization has been used.

## Slide 15: Parameters

## Slide 16
Soil parameter look up by zone code
STATSGO Soil derived parameters
Soil texture for each of the 11 standard soil depth grid layers from PSU gridding of NRCS STATSGO data.
Table of Soil Hydraulic Properties – Clapp Hornberger 1978
Depth weighted average
Exponential decrease with depth
…
Soil Grid Layers
Joined to Polygon Layer
q1 ,, q2 , & yf
f & K
Zone Code Polygon Layer

## Slide 17
Vegetation derived parameters
NASA LDAS vegetation database
IGBP Classification
1-km AVHRR imagery

## Slide 18
Specific catchment area using D algorithm used to compute wetness index
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)
Digital Elevation Model Derived Parameters

## Slide 19
Basin 1
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.05
0.10
0.15
0.20
Basin 3
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 2
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
25
0.00
0.10
0.20
Basin 4
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
0.30
Basin 7
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 8
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 6
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.10
0.20
Basin 9
ln(a/S) (a in meter units)
Proportion of area
0
5
10
15
20
0.00
0.05
0.10
0.15
0.20
Wetness index histogram for each subwatershed used to parameterize subgrid variability of soil moisture

## Slide 20
Global probabilistic search using Shuffled Complex Evolution algorithm implemented in NLFIT (Kuczera, 1994, 1997)
Parameter multipliers to K, f, n, Cr, v
Calibration period 971001-990531
~ 1 graduate student week on calibration – essentially just letting the algorithm run till minimal improvement for each watershed
Calibration
Kuczera, G., (1994), "NLFIT, A Bayesian Nonlinear Regression Program Suite," Version 1.00g, Department of Civil Engineering and Surveying, University of Newcastle, NSW, 2308, Australia.
Kuczera, G., (1997), "Efficient Subspace Probabilistic Parameter Optimization for Catchment Models," Water Resources Research, 33(1): 177-185.

## Slide 21
Parameter multiplier results after optimization
"Uncalibrated" parameter multipliers
Notes: Parameter constraints - Min then Max
0 1.e+20 Area (not a var1able parameter)
1.0 15.0 f
0.001 150. k
0.01 0.4 dtheta1
0.05 0.4 dtheta2
0.005 2.00 soilmc
0.0 20.0 exp c
0.0 0.5 psif
1. 10000. Overland flow velocity
0.0 0.005 Canopy capacity
0.0 2.0 Evap enhancement factor,cr
0.0 1.0 Albedo
0.0 1.0 Lapse rate (not a var1able parameter)
0.0 1.e+5 Sub-basin elevation (not a var1able parameter)
Initial condition constraints - Min then Max
0.0 2.0 Initial soil moisture
-0.5 5.0 Initial depth to WT
0.0 0.005 Initial canopy storage
Reach parameter constraints - Min then Max
0.0001 1.0 Channel slope (not a var1able parameter)
0.001 2.0 Manning's 'n'
0.1 1.e+07 Channel width (not a var1able parameter)
10000. 1.e+10 Channel length (not a var1able parameter)

## Slide 22
Run time issues:
System: AMD Athlon XP 1900+
512 MB RAM
Platform: Windows 2000
Run-time for one model run
63000 timesteps: 4-9 minutes
Model elements: 9-21
Parameter Calibration by SCE
Five parameters: 6-9+ hours

## Slide 23
Some Results
Baron Cumulative Water Balance

## Slide 24
Basin specific Model Outputs for two Baron 1995 events
Depth to water table
Saturation excess runoff
Infiltration excess runoff
Unsat.
soil zone store

## Slide 25
Modeling results

## Slide 27
Chart: Nash-Sutcliffe Measure for Daily Volume
| Baron | Blue | Elk | Tahl | Watt
Uncalibrated | 0.55386 | 0.42764 | -0.050189 | 0.54402 | 0.30969
Calibrated | 0.73268 | 0.6309 | 0.54322 | 0.74448 | 0.70693
Chart: Nash-Sutcliffe Measure for Hourly Flow
| Baron | Blue | Elk | Tahl | Watt
Uncalibrated | 0.49632 | 0.3981 | -0.015319 | 0.50816 | 0.30571
Calibrated | 0.66946 | 0.56345 | 0.52175 | 0.71371 | 0.67104

## Slide 28
Changes in the slope of the cumulative runoff/cumulative rainfall ratio
used to diagnose biases either in streamflow
or precipitation measurement, most likely precipitation.
Oct,1,1993
Oct,1,1999
0.48
0.42
0.14
0.26
0.25
0.50
0.50
0.20
0.44
0.46
0.48

## Slide 30
DMIP Annual Runoff Ratios

## Slide 31
Lessons Learned
DMIP Data
Data exhibits changing annual runoff ratio with relatively higher observed flow in years with smaller precipitation and visa versa. We believe this is most likely due to biases in the precipitation input. Calibration to attempt to match this is unreasonable.
Our model
A simple exponential functional form of baseflow response, , limits the capability of the model to match recessions in both low and high flow conditions.
Fitting to mse doesn’t help with cumulative mass balance. Need to consider use of cumulative time series in calibration.
Future work
Model element scale questions
Connections between calibrated parameters and soil and veg attributes
Alternative generalized baseflow storage – discharge functions
Decouple K in soil and saturated store
Add impervious areas
Add snow