## Slide 1: Hydrologic Terrain Analysis in ArcGIS
David G. Tarboton
dtarb@cc.usu.edu
http://www.engineering.usu.edu/dtarb

## Slide 2: Outline
Grid based terrain flow data model
Objective stream threshold delineation
Variable drainage density
D multiple flow direction model
Flow algebra
Terrain stability mapping (SINMAP)

## Slide 3: Terrain Data Models
Grid
Contour and flowline
TIN

## Slide 4: Duality between Terrain and Drainage Network
Flowing water erodes landscape and carries away sediment sculpting the topography
Topography defines drainage direction on the landscape and resultant runoff and streamflow accumulation processes

## Slide 5: Grid based terrain flow data model
A grid defines geographic space as a matrix of identically-sized square cells. Each cell holds a numeric value that measures a geographic attribute (like elevation) for that unit of space.

## Slide 6
4
5
6
3
7
2
1
8
Eight Direction Pour Point Model D8
Slope = Drop/Distance
Steepest down slope direction
67
56
49
52
48
37
58
55
22
30

## Slide 7: Grid based terrain flow data model
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
3
3
12
2
2
2
3
16
25
6
Drainage Area
4
5
6
3
7
2
1
8
Eight direction pour point model D8
Grid network

## Slide 8
0
0
0
0
0
0
0
0
0
0
0
0
0
0
3
2
2
11
1
1
15
2
5
24
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
3
2
2
11
1
1
1
2
15
24
5
Flow Accumulation Grid.
Area draining in to a grid cell
ArcHydro Page 72

## Slide 9: Flow Accumulation > 5 Cell Threshold
0
0
0
0
0
0
0
0
0
0
0
0
0
0
3
2
2
11
1
1
15
2
5
24
1
Channel or Stream Raster

## Slide 10: Watershed delineated on a topographic map

## Slide 11
5
5
1
1
1
3
2
2
3
3
4
4
4
4
4
5
5
6
6
6
Stream Segments in a Grid Cell Network

## Slide 12
ArcHydro Page 74
Stream links grid for the San Marcos subbasin
172
201
204
202
206
203
209
Each link has a unique identifying number

## Slide 13: Catchments
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape through a set of physical rules

## Slide 14: Delineation of Channel Networks and Catchments
500 cell theshold
1000 cell theshold

## Slide 15: How to decide on stream delineation threshold ?
AREA 1
AREA 2
3
12
Why is it important?

## Slide 16
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in models.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.
Objective determination of channel network drainage density

## Slide 17
“landscape dissection into distinct valleys is limited by a threshold of channelization that sets a finite scale to the landscape.” (Montgomery and Dietrich, 1992, Science, vol. 255 p. 826.)
One contributing area threshold does not fit all watersheds.
Map stream networks from the DEM at the finest resolution consistent with observed stream network geomorphology ‘laws’.

## Slide 18: Strahler Stream Order
Order 1
Order 2
most upstream is order 1
when two streams of a order i join, a stream of order i+1 is created
when a stream of order i joins a stream of order i+1, stream order is unaltered
Order 3
Order 4
Order 5

## Slide 19: Constant Stream Drops Law
Broscoe, A. J., (1959), "Quantitative analysis of longitudinal stream profiles of small watersheds," Office of Naval Research, Project NR 389-042, Technical Report No. 18, Department of Geology, Columbia University, New York.

## Slide 20: Stream Drop Elevation difference between ends of stream
Note that a “Strahler stream” comprises a sequence of links (reaches or segments) of the same order
Nodes
Links
Single Stream

## Slide 21: Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
Look for statistically significant break in constant stream drop property
Break in slope versus contributing area relationship
Physical basis in the form instability theory of Smith and Bretherton (1972), see Tarboton et al. 1992

## Slide 22: Statistical Analysis of Stream Drops
Chart: Elevation Drop for Streams
Mean Drop | 72.2322 | 122.7541 | 142.0625 | 221

## Slide 23: T-Test for Difference in Mean Values
72
130
0
T-test checks whether difference in means is large (> 2)
when compared to the spread of the data around the mean values

## Slide 24: Statistical Analysis of Stream Drops

## Slide 25
200 grid cell constant drainage area based stream delineation

## Slide 26
100 grid cell constant drainage area threshold stream delineation

## Slide 27: Local Curvature Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58

## Slide 28: Contributing area of upwards curved grid cells only

## Slide 29: Upward Curved Contributing Area Threshold

## Slide 30
Curvature based stream delineation with threshold by constant drop analysis

## Slide 31: Channel network delineation, other options
4
5
6
3
7
2
1
8
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
3
3
12
2
2
2
3
16
25
6
Contributing Area
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
3
1
1
1
2
3
3
2
Grid Order

## Slide 32: Grid Network Ordering Approach (Peckham, 1995)

## Slide 33
Grid network pruned to order 4 stream delineation

## Slide 34: Slope area threshold (Montgomery and Dietrich, 1992).

## Slide 35: Limitation due to 8 grid directions.
?
Flow Direction Field — if the elevation surface is differentiable (except perhaps for countable discontinuities) the horizontal component of the surface normal defines a flow direction field.

## Slide 36
D Multiple flow direction model
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)

Proportion flowing to neighboring grid cell 1 is 2/(1 + 2)
Proportion flowing to neighboring grid cell 2 is 1/(1 + 2)

## Slide 37
Contributing Area using D8
Contributing Area using D

## Slide 38
Flow Algebra

## Slide 39
Useful for example to track where sediment or contaminant moves

## Slide 40
Useful for example to track where a contaminant may come from

## Slide 41
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 42
Useful for a tracking a contaminant released or partitioned to flow at a fixed threshold concentration

## Slide 43: Transport limited accumulation
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment

## Slide 44: Terrain Stability Mapping
With Bob Pack. http://www.engineering.usu.edu/dtarb/sinmap.htm

## Slide 45: SINMAP Theoretical Basis
q = slope
Infinite Plane Slope Stability Model
FS=Factor of Safety
where
R
D
Dw
D
h
Density Ratio
Relative Wetness
Dimensionless Cohesion
= DEM source

## Slide 46: DEM Governs Slope & Flow Accumulation
Flow Accumulation (a)
Slope (θ)
DTM Quality
Digital Terrain Model (DTM)

## Slide 47: Probabilistic Formulation
MODEL
P(FS>1)
Flow Accumulation
Slope
Shear Strength
Wetness
Soil/Root Cohesion
SI=FS &

## Slide 48: Stability Class Definitions
1.0

## Slide 49: Interactive Calibration
Selection of ranges of Φ, R/T & c moves position of stability class breaks
Selection of range of R/T moves position of wetness class breaks

## Slide 50
SLOPE
DRAINAGE AREA UPSLOPE
SATURATED
STABLE
UNSTABLE
UNSATURATED
Example Result – Foster Ck
Class 1
2
3
4
5
6

## Slide 51
Foster Creek SI Map

## Slide 52
LANDSLIDE DENSITIES & AREAS FOR SI CLASSES

## Slide 53
Reverse Accumulation
Useful for destabilization sensitivity in landslide hazard assessment
With Bob Pack

## Slide 54: Most Likely Initiation Points
The location of the lowest SI value along a flow path
With Paolo Tarolli, University of Padova
http://www.copernicus.org/EGU/hess/hessd/3/395/hessd-3-395.pdf

## Slide 56
With Paolo Tarolli, University of Padova
http://www.copernicus.org/EGU/hess/hessd/3/395/hessd-3-395.pdf

## Slide 57
Concluding Point
The GIS grid based terrain flow data model enables the representation of flow processes at and near the earth surface and derivation of a wide variety of information useful for the study of hydrologic processes.

## Slide 58: Questions?
AREA 1
AREA 2
3
12
TauDEM and SINMAP available at: http://www.engineering.usu.edu/dtarb