## Slide 1: Terrain Analysis Using Digital Elevation Models (TauDEM) in Hydrology
David G. Tarboton
dtarb@cc.usu.edu
http://www.engineering.usu.edu/dtarb

## Slide 2: Overview
Review of digital elevation model grid based flow direction, accumulation and watershed delineation
Channel network delineation. Objective selection of channel delineation threshold and representation of variable drainage density.
Terrain flow fields and their numerical representation. Multiple flow direction approaches.
Specialized grid accumulation functions

## Slide 3: Elevation Surface — the ground surface elevation at each point
Digital Elevation Model — A digital representation of an elevation surface. Examples include a (square) digital elevation grid, triangular irregular network, set of digital line graph contours or random points.

## Slide 4: Digital Elevation Model Based Flow Path Analysis
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
3
3
12
2
2
2
3
16
25
6
Drainage Area
4
5
6
3
7
2
1
8
Eight direction pour point model D8
Grid network
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
3
1
1
1
2
3
3
2
Grid Order

## Slide 5
100 grid cell constant support area threshold stream delineation

## Slide 6
Grid network pruned to order 4 stream delineation

## Slide 7
200 grid cell constant support area based stream delineation

## Slide 8: How to decide on drainage area threshold ?
AREA 1
AREA 2
3
12
Why is it important?

## Slide 9
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in models.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.
Objective determination of channel network drainage density

## Slide 10: Delineation of Channel Networks and Subwatersheds
500 cell theshold
1000 cell theshold

## Slide 11: Examples of differently textured topography
Same scale, 20 m contour interval
Sunland, CA
Driftwood, PA

## Slide 12: Logged Pacific Redwood Forest near Humboldt, California

## Slide 13: Gently Sloping Convex Landscape
From W. E. Dietrich

## Slide 14: Mancos Shale badlands, Utah. From Howard, 1994.

## Slide 15
Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
“landscape dissection into distinct valleys is limited by a threshold of channelization that sets a finite scale to the landscape.” (Montgomery and Dietrich, 1992, Science, vol. 255 p. 826.)
One contributing area threshold does not fit all watersheds.

## Slide 16: Constant Stream Drops Law based on Strahler Stream Ordering
Broscoe, A. J., (1959), "Quantitative analysis of longitudinal stream profiles of small watersheds," Office of Naval Research, Project NR 389-042, Technical Report No. 18, Department of Geology, Columbia University, New York.
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
3

## Slide 17: Stream Drop Elevation difference between ends of stream
Note that a “Strahler stream” comprises a sequence of links (reaches or segments) of the same order
Nodes
Links
Single Stream

## Slide 18: Statistical Analysis of Stream Drops
Chart: Elevation Drop for Streams
Mean Drop | 72.2322 | 122.7541 | 142.0625 | 221

## Slide 19: Constant Support Area Threshold

## Slide 20
200 grid cell constant support area based stream delineation

## Slide 21: Local Curvature Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58

## Slide 22: Contributing area of upwards curved grid cells only

## Slide 23: Upward Curved Contributing Area Threshold

## Slide 24
Curvature based stream delineation

## Slide 25: Topographic Slope
?
Topographic Definition Drop/Distance
Limitation imposed by 8 grid directions.

## Slide 26
The D Algorithm
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)

## Slide 27
Contributing Area using D8
Contributing Area using D

## Slide 29
Useful for example to track where sediment or contaminant moves

## Slide 30
Useful for example to track where a contaminant may come from

## Slide 31
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 32
Useful for a tracking a contaminant released or partitioned to flow at a fixed threshold concentration

## Slide 33: Transport limited accumulation
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment

## Slide 34
Reverse Accumulation
Useful for destabilization sensitivity in landslide hazard assessment
with Bob Pack

## Slide 35: Why Programming

## Slide 36: TauDEM Software Functionality
Pit removal (standard flooding approach)
Flow directions and slope
  D8 (standard)
  D (Tarboton, 1997, WRR 33(2):309)
  Flat routing (Garbrecht and Martz, 1997, JOH 193:204)
Drainage area (D8 and D)
Network and watershed delineation
  Support area threshold/channel maintenance coefficient (Standard)
  Combined area-slope threshold (Montgomery and Dietrich, 1992, Science, 255:826)
  Local curvature based (using Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
Threshold/drainage density selection by stream drop analysis (Tarboton et al., 1991, Hyd. Proc. 5(1):81)
Other Functions: Downslope Influence, Upslope Dependence, Wetness index, distance to streams, Transport limited accumulation

## Slide 37: TauDEM in ArcGIS
ESRI binary
grid
ASCII text
grid
ESRI gridio API
(Spatial analyst)
USU TMDLtoolkit modules
(grid, shape, image, dbf, map, mapwin)
TauDEM C++ library
Fortran (legacy)
components
Standalone
command line
applications
C++ COM DLL interface
Visual Basic
GUI
application
Visual Basic
ESRI ArcGIS 8.x
Toolbar
Vector shape
files
Data
formats
Available from
http://www.engineering.usu.edu/dtarb/
Binary direct
access grid

## Slide 38: Are there any questions ?
AREA 1
AREA 2
3
12
http://www.engineering.usu.edu/dtarb