## Slide 1: Developing a Community Hydrologic Information System
David G Tarboton
David R. Maidment (PI)
Ilya Zaslavsky
Michael Piasecki
Jon Goodall
Graduate students, programmers and collaborators: Jeff Horsburgh, David Valentine, Tim Whiteaker, Bora Beran, Ernest To, Tim Whitenack, Dean Djokic, Zhumei Qian
http://www.cuahsi.org/his.html
Support
EAR 0622374
EAR 0413265

## Slide 2: Outline
The CUAHSI HIS
Web Services
Observations Data Model
Observatory Test Bed Implementation

## Slide 3: CUAHSI HIS Goals
better Data Access
support for Hydrologic Observatories
advancement of Hydrologic Science
enabling Hydrologic Education
Space
Time
Variables
Value

## Slide 4
Rainfall & Snow
Water quantity and quality
Remote sensing
Water Data
Modeling
Meteorology
Soil water

## Slide 5
Provide access to multiple heterogeneous data sources simultaneously regardless of semantic or structural differences between them
Objective
NWIS
NARR
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
What we are doing now …..
Slide from Michael Piasecki, Drexel University

## Slide 6
What we would like to do …..
NWIS
NAWQA
NARR
generic
request
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
ODM
Slide from Michael Piasecki, Drexel University

## Slide 7
WaterOneFlow Web Services
Data access through web services
Data storage through web services
Downloads
Uploads
Observatory data servers
CUAHSI HIS data servers
3rd party data servers
e.g. USGS, NCDC
GIS
Matlab
IDL
Splus, R
Excel
Programming (Fortran, C, VB)
Web services interface
Hydrologic Data Access System Website Portal and Map Viewer
Information input, display, query and output services
Preliminary data exploration and discovery. See what is available and perform exploratory analyses
HTML -XML
WSDL - SOAP
ODM
ODM
Notes: Hydrologic Information System Service Oriented Architecture

## Slide 8: CUAHSI Hydrologic Data Access System (HDAS)
A common data window for accessing, viewing and downloading hydrologic information
USGS
NASA
NCDC
EPA
NWS
Observatory Data

## Slide 9: Outline
The CUAHSI HIS
Web Services
Observations Data Model
Observatory Test Bed Implementation

## Slide 10
NWIS
ArcGIS
Excel
NCAR
Unidata
NASA
Storet
NCDC
Ameriflux
Matlab
Access
Java
Fortran
Visual Basic
C/C++
Some operational services
CUAHSI Web Services
Data Sources
Applications
Extract
Transform
Load
http://www.cuahsi.org/his.html

## Slide 11: Example: Matlab use of CUAHSI Web Services
% create NWIS Class and an instance of the class
createClassFromWsdl('http://water.sdsc.edu/wateroneflow/NWIS/DailyValues.asmx?WSDL');
WS = NWISDailyValues;
% Site Info for Site of Interest
siteid='NWIS:02087500';
strSite=GetSiteInfoObject(WS,siteid,'');
strSite.site.siteInfo.siteName
ans =
NEUSE RIVER NEAR CLAYTON, NC
lat=strSite.site.siteInfo.geoLocation.geogLocation.lat itude
long=strSite.site.siteInfo.geoLocation.geogLocation.longitude
lat =
35.6472222
long =
-78.4052778

## Slide 12: Variable and variableTimeInterval
strSite.site.seriesCatalog(1).series(:).variable
ans =
variableCode: '00065'
variableName: 'Gage height, feet'
units: 'international foot'
ans =
variableCode: '00060'
variableName: 'Discharge, cubic feet per second'
units: 'cubic feet per second'
strSite.site.seriesCatalog(1).series(:).variableTimeInterval
ans =
beginDateTime: '1927-08-01T00:00:00'
endDateTime: '2006-10-16T00:00:00'
ans =
beginDateTime: '1927-08-01T00:00:00'
endDateTime: '2006-10-16T00:00:00'

## Slide 13: getVariableInfo
varcode='NWIS:00060';
varInfo=GetVariableInfoObject(WS,varcode,'')
varInfo =
variables: [1x1 struct]
varInfo.variables.variable
ans =
variableCode: '00060'
variableName: 'Discharge, cubic feet per second'
units: 'cubic feet per second'

## Slide 14: GetValues
% GetValues to get the data
siteid='NWIS:02087500';
bdate='2002-09-30T00:00:00';
edate='2006-10-16T00:00:00';
variable='NWIS:00060';
valuesxml=GetValues(WS,siteid,variable,bdate,edate,'');

## Slide 15: Parse XML and Analyze
% Parse the XML into a Matlab object to work with
valuesobj=xml_parseany(valuesxml);
...
plot(date,flowval);datetick;

## Slide 16: Outline
The CUAHSI HIS
Web Services
Observations Data Model
Observatory Test Bed Implementation

## Slide 17: Hydrologic Science
Hydrologic conditions
(Fluxes, flows, concentrations)
Hydrologic Process Science
(Equations, simulation models, prediction)
Hydrologic Information Science
(Observations, data models, visualization
Hydrologic environment
(Dynamic earth)
Physical laws and principles
(Mass, momentum, energy, chemistry)
It is as important to represent hydrologic environments precisely with
data as it is to represent hydrologic processes with equations

## Slide 18: Continuous Space-Time Model – NetCDF (Unidata)
Space, L
Time, T
Variables, V
D
Coordinate
dimensions
{X}
Variable dimensions
{Y}

## Slide 19: Discrete Space-Time Data Model ArcHydro
Space, FeatureID
Time, TSDateTime
Variables, TSTypeID
TSValue

## Slide 20: Terrain Data Models
Grid
Contour and flowline
TIN

## Slide 21: CUAHSI Observations Data Model
A relational database at the single observation level (atomic model)
Stores observation data made at points
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Standard format for data sharing
Cross dimension retrieval and analysis
Streamflow
Flux tower
data
Precipitation
& Climate
Groundwater
levels
Water Quality
Soil
moisture
data

## Slide 22: Scope
Focus on Hydrologic Observations made at a point
Exclude remote sensing or grid data. These are part of a digital watershed but not suitable for an atomic database model and individual value queries
Primarily store raw observations and simple derived information to get data into its most usable form.
Limit inclusion of extensively synthesized information and model outputs at this stage.

## Slide 23: What are the basic attributes to be associated with each single data value and how can these best be organized?
Value
DateTime
Variable
Location
Units
Interval (support)
Accuracy
Offset
OffsetType/ Reference Point
Source/Organization
Censoring
Data Qualifying Comments
Method
Quality Control Level
Sample Medium
Value Type
Data Type

## Slide 25: Site Attributes
SiteCode, e.g. NWIS:10109000
SiteName, e.g. Logan River Near Logan, UT
Latitude, Longitude Geographic coordinates of site
LatLongDatum Spatial reference system of latitude and longitude
Elevation_m Elevation of the site
VerticalDatum Datum of the site elevation
Local X, Local Y Local coordinates of site
LocalProjection Spatial reference system of local coordinates
PosAccuracy_m Positional Accuracy
State, e.g. Utah
County, e.g. Cache

## Slide 26
Feature
Waterbody
HydroID
HydroCode
FType
Name
AreaSqKm
JunctionID
HydroPoint
HydroID
HydroCode
FType
Name
JunctionID
Watershed
HydroID
HydroCode
DrainID
AreaSqKm
JunctionID
NextDownID
ComplexEdgeFeature
EdgeType
Flowline
Shoreline
HydroEdge
HydroID
HydroCode
ReachCode
Name
LengthKm
LengthDown
FlowDir
FType
EdgeType
Enabled
SimpleJunctionFeature
1
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
*
1
*
HydroNetwork
*
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
1
1
CouplingTable
SiteID
HydroID
Sites
SiteID
SiteCode
SiteName
Latitude
Longitude
…
Observations Data Model
1
1
OR
Independent of, but can be coupled to Geographic Representation
ODM
Arc Hydro

## Slide 27: Variable attributes
VariableName, e.g. discharge
VariableCode, e.g. NWIS:0060
SampleMedium, e.g. water
ValueType, e.g. field observation, laboratory sample
IsRegular, e.g. Yes for regular or No for intermittent
TimeSupport (averaging interval for observation)
DataType, e.g. Continuous, Instantaneous, Categorical
GeneralCategory, e.g. Climate, Water Quality
NoDataValue, e.g. -9999
m3/s
Flow
Cubic meters per second

## Slide 28: Scale issues in the interpretation of data
The scale triplet
From: Blöschl, G., (1996), Scale and Scaling in Hydrology, Habilitationsschrift, Weiner Mitteilungen Wasser Abwasser Gewasser, Wien, 346 p.
a) Extent
b) Spacing
c) Support

## Slide 29
From: Blöschl, G., (1996), Scale and Scaling in Hydrology, Habilitationsschrift, Weiner Mitteilungen Wasser Abwasser Gewasser, Wien, 346 p.

## Slide 30: Discharge, Stage, Concentration and Daily Average Example

## Slide 31: Data Types
Continuous (Frequent sampling - fine spacing)
Sporadic (Spot sampling - coarse spacing)
Cumulative
Incremental
Average
Maximum
Minimum
Constant over Interval
Categorical

## Slide 32: 15 min Precipitation from NCDC
Incomplete or Inexact daily total occurring. Value is not a true 24-hour amount. One or more periods are missing and/or an accumulated amount has begun but not ended during the daily period.
Notes: NCDC Precipitation Example
Concepts:
Use of nodata value in Value field of Values table (denotes beginning and ending of a no data period)
Multiple observations of multiple variables at a single site
Storage of incremental data with different time support (15 minute incremental vs. 24 hour incremental)
Use of data qualifying comments
Use of end of interval accumulation of data (the sum of precipitation for a day is reported at the end of the day – midnight of the next day)
Relationships:

## Slide 33: Irregularly sampled groundwater level
Notes: Groundwater Level Example
Concepts:
Multiple observations of a single variable at a single site made by a single source
Use of a quality control level to qualify data
Relationships:
Relationship between the Sites table and the Values table on SiteID
Relationship between the Values table and the Variables table on VariableID
Relationship between the Values table and the Sources table on SourceID
Relationship between the Values table and the QualityControlLevelDefinitions table on QualityControlLevel

## Slide 34: Offset
OffsetValue
Distance from a datum or control point at which an observation was made
OffsetType defines the type of offset, e.g. distance below water level, distance above ground surface, or distance from bank of river

## Slide 35: Water Chemistry from a profile in a lake
Notes: Water Chemistry From a Lake Profile
Concepts:
Grouped observations (all observations in one reservoir profile)
Observations made using an offset (observations made at multiple depths below the surface of a reservoir)
Observations made using a specific method (observations made using a particular field instrument)
Relationships:
Relationship between Values table and the Variables table on VariableID
Relationship between Values table and OffestTypes table on OffsetTypeID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID
Relationship between GroupDescriptions table and Groups table on GroupID
Relationship between OffsetTypes table and Units table on UnitID and OffsetUnitID

## Slide 36: Groups and Derived From Associations

## Slide 37: Stage and Streamflow Example
Notes: Discharge Derived from Gage Height
Concepts:
Data derived from other data – single data point derived from a single observation (discharge from stage)
Data derived using a specific method (discharge from stage using rating curve)
Relationships:
Relationships between Values table and DerivedFrom table on DerivedFromID and ValueID
Relationship between Values table and Variables table on VariableID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID

## Slide 38: Daily Average Discharge Example Daily Average Discharge Derived from 15 Minute Discharge Data
Notes: Daily Average Discharge Derived from 15 Minute Discharge Data
Concepts:
Data derived from other data – single data point derived from multiple observations (daily average from 15 minute instantaneous observations)
Data derived using a method (daily average by averaging 15 minute instantaneous observations)
Relationships:
Relationship between Values table and DerivedFrom table on DerivedFromID
Relationship between Values table and Methods table on MethodID
Relationship between Values table and Variables table on VariableID
Relationship between Variables table and Units table on UnitID

## Slide 39: Methods and Samples
Method specifies the method whereby an observation is measured, e.g. Streamflow using a V notch weir, TDS using a Hydrolab, sample collected in auto-sampler
SampleID is used for observations based on the laboratory analysis of a physical sample and identifies the sample from which the observation was derived. This keys to a unique LabSampleID (e.g. bottle number) and name and description of the analytical method used by a processing lab.

## Slide 40: Water Chemistry from Laboratory Sample

## Slide 41
ValueAccuracy
A numeric value that quantifies measurement accuracy defined as the nearness of a measurement to the standard or true value. This may be quantified as an average or root mean square error relative to the true value. Since the true value is not known this may should be estimated based on knowledge of the method and measurement instrument. Accuracy is distinct from precision which quantifies reproducibility, but does not refer to the standard or true value.
Accurate
Low Accuracy, but precise
Low Accuracy
ValueAccuracy
Bias

## Slide 42: Data Quality and Processing Levels
Qualifier Code and Description provides qualifying information about the observations, e.g. Estimated, Provisional, Derived, Holding time for analysis exceeded
QualityControlLevel records the level of quality control that the data has been subjected to. - Level 0. Raw Data - Level 1. Quality Controlled Data - Level 2. Derived Products - Level 3. Interpreted Products - Level 4. Knowledge Products

## Slide 43: Series of Observations
A “Data Series” is a set of all the observations of a particular variable at a site.
The SeriesCatalog is programmatically generated to provide users with the ability to do data discovery (i.e. what data is available and where) without formulating complex queries or hitting the DataValues table which can get very large.

## Slide 44: Outline
The CUAHSI HIS
Web Services
Observations Data Model
Observatory Test Bed Implementation

## Slide 45: Workgroup HIS Server

## Slide 46: Automated Ingestion of Sensor Data into ODM
Observations
Database
(ODM)
Base Station
Computer(s)
Data Processing
Applications
Telemetry Network
Sensors
Internet
Challenges
Heterogeneity
Establishing standards
  Sensor/system descriptions Sensor ML

## Slide 47: ODM and HIS in an Observatory Setting Integration of Sensor Data With HIS
Observations
Database
(ODM)
Base Station
Computer(s)
Data Processing
Applications
Internet
Telemetry Network
Sensors
Data discovery, visualization, analysis, and modeling through Internet enabled applications
Programmer interaction through web services
Internet
Workgroup HIS Tools
Workgroup HIS
Server

## Slide 48: Managing Data Within ODM - ODM Tools
Load – import existing data directly to ODM
Query and export – export data series and metadata
Visualize – plot and summarize data series
Edit – delete, modify, adjust, interpolate, average, etc.

## Slide 49
Chart: Little Bear River Near Avon (4905700)
Chart: Little Bear River at Mendon Road (4905000)
Bayesian Networks to construct water quality measures from surrogate sensor signals to provide high frequency estimates of water quality and loading
Site specific correlations
between sensor signals
and other water quality variables
Sensors, data collection, and telemetry network
Bayesian Networks to control monitoring system, triggering sampling for storm events and base flow
CUAHSI HIS ODM – central storage and management of observations data
End result: high frequency estimates of nutrient concentrations and loadings
Integrated Monitoring System

## Slide 50: Conclusion Advancement of water science is critically dependent on integration of water information
Databases: Structured data sets to facilitate data integrity and effective sharing and analysis.
- Standards
- Metadata
- Unambiguous interpretation
Analysis: Tools to provide windows into the database to support visualization, queries, analysis, and data driven discovery.
Models: Numerical implementations of hydrologic theory to integrate process understanding, test hypotheses and provide hydrologic forecasts.
Databases
Analysis
Models
ODM
Web Services

## Slide 51: Questions?
AREA 1
AREA 2
3
12