## Slide 1: The CUAHSI Community Hydrologic Information System
David Tarboton, David Maidment, Ilya Zaslavsky, Dan Ames, Jon Goodall, Richard Hooper, Jeffery Horsburgh
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/

## Slide 2: Hydrologic Data Challenges
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
Data Heterogeneity
The way that data is organized can enhance or inhibit the analysis that can be done

## Slide 3: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 4: CUAHSI Hydrologic Information System Services-Oriented Architecture
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
ODM
Geo Data
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards
Information Model and Community Support Infrastructure

## Slide 5: What are the basic attributes to be associated with each single data value and how can these best be organized?
Space, S
Time, T
Variables, V
s
t
Vi
vi (s,t)
“Where”
“What”
“When”
A data value
Variable
Method
Quality Control Level
Sample Medium
Value Type
Data Type
Source/Organization
Units
Accuracy
Censoring
Qualifying comments
Location
Feature of interest
Latitude
Longitude
Site identifiers
DateTime
Interval (support)

## Slide 6: Observations Data Model (ODM)
Soil
moisture
data
Streamflow
Flux tower data
Groundwater
levels
Water Quality
Precipitation
& Climate
A relational database at the single observation level
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Promote syntactic and semantic consistency
Cross dimension retrieval and analysis
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, doi:10.1029/2007WR006392.
Provides a common persistence model for data storage

## Slide 7
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
GetSites
WaterOneFlow
Web Service
GetValues
GetSiteInfo
GetVariableInfo
Notes: 7

## Slide 8: HydroServer – Data Publication
Ongoing Data Collection
Data presentation, visualization, and analysis through Internet enabled applications
Internet Applications
Point Observations Data
Historical Data Files
GIS Data
ODM Database
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
OGC Spatial Data Service from ArcGIS Server
Notes: A platform for publishing space-time hydrologic datasets that:
  Autonomous with local control of data
  Part of a distributed system that makes data universally available
Basis for Experimental Watershed or Observatory data management system
Standards based approach to data publication
  Accepted and emerging standards for data storage and transfer (OGC, WaterML)
Built on established software
  MS SQL Server, ArcGIS server
Open Source Community Code Repository
  Sustainability

## Slide 9
HydroCatalog
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
Discovery and Access
Hydro
Desktop
Water Metadata Catalog
Harvester
Service Registry
Hydrotagger
Search Services
http://hiscentral.cuahsi.org
Search over data services from multiple sources
Supports concept based data discovery
CUAHSI Data Server
3rd Party Server
e.g. USGS

## Slide 10: Thematic keyword search
Integration from multiple sources
Search on space and time domain
HydroDesktop – Data Access and Analysis

## Slide 11
Integration with “R” Statistics Package

## Slide 12: Open Geospatial Consortium Web Service Standards
Map Services
Web Map Service (WMS)
Web Feature Service (WFS)
Web Coverage Service (WCS)
Catalog Services for the Web (CS/W)
Observation Services
Observations and Measurements Model
Sensor Web Enablement (SWE)
Sensor Observation Service (SOS)
These standards have been developed over the past 10 years ….
…. by 400 companies and agencies working within the OGC
OGC Hydrology Domain Working Group evolving WaterML into an International Standard
http://www.opengeospatial.org/projects/groups/waterml2.0swg

## Slide 13: A growing collection of HydroServers and community of users
Dry Creek Experimental Watershed (DCEW) (28 km2 semi-arid steep topography, Boise Front)
68 Sites
24 Variables
4,700,000+ values
Published by Jim McNamara, Boise State University
University of Maryland, Baltimore County
Montana State University
University of Texas at Austin
University of Iowa
Utah State University
University of Florida
University of New Mexico
University of Idaho
Boise State University
University of Texas at Arlington
University of California, San Diego
Idaho State University

## Slide 14: Open Development Model
http://hydrodesktop.codeplex.com
http://hydroserver.codeplex.com
http://hydrocatalog.codeplex.com

## Slide 15: General aspects of the approach
Storage in a community data model
Publication from a server
Data access through internet-based services using consistent language and format
Tools for access and analysis
Discovery through thematic and geographic search functionality
Integrated modeling and analysis combining information from multiple sources
Discovery and Integration
Data Services
Catalog
Synthesis and Research
Desktop/Client
Publication
Server
Metadata Services
Search Services
Standards
Information Model and Community Support Infrastructure
Accessibility
Discoverability
Consumability
Common functional components

## Slide 16: Looking to the Future
Move from prototype to operations
  Operational support of software and systems
  User support and training
  Repositories
  CUAHSI Data Center (User Solutions Engineer)
  NSF Data Management Requirements
Research and development of new functionality
  data and model sharing “hub” to enhance interactive collaboration (pending)
Community
  HIS has become bigger than one project (emerging software ecosystem)
  Open Development Model (inspire, enable and incorporate broad contributions)
  The community is the infrastructure that persists (is sustainable)

## Slide 17: Thanks! HIS Project Team and Sponsors
University of Texas at Austin – David Maidment, Tim Whiteaker, James Seppi, Fernando Salas, Jingqi Dong, Harish Sangireddy
San Diego Supercomputer Center – Ilya Zaslavsky, David Valentine, Tom Whitenack, Matt Rodriguez
Utah State University – David Tarboton, Jeff Horsburgh, Kim Schreuders, Stephanie Reeder
University of South Carolina – Jon Goodall, Anthony Castronova
Idaho State University – Dan Ames, Ted Dunsford, Jiří Kadlec, Yang Cao, Dinesh Grover
Drexel University/CUNY – Michael Piasecki
WATERS Network – Testbed Data Managers
CUAHSI Program Office – Rick Hooper, Yoori Choi, Conrad Matiuk
ESRI – Dean Djokic, Zichuan Ye
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/