## Slide 1: What makes the Great Salt Lake level go up and down ?
Utah Water Research Laboratory, Utah State University, Logan, Utah1.
Earth & Environmental Eng, Columbia University2.
GSA presentation, Salt Lake City, Utah, USA, Oct. 17, 2005
Tarboton, David G.1.
Mohammed, Ibrahim N.1.
Lall, Upmanu2.

## Slide 2: Great Salt Lake Basin Hydrologic Observatory
Bear
West Desert
Jordan/Provo
Weber
Strawberry
A Hydrologic Observatory to advance understanding of water resources in the modern west

## Slide 3: A microcosm for many "western" water issues
Climate Gradients (Snow fed, Alpine to semi-arid), variability and vulnerability
Topographic and Land Use Gradients
Mountain Front / Valley groundwater dynamics and interactions
Geologic Diversity (Granite to Karst)
Closed basin for water and constituent balance closure
Development issues (local growth, SLC metropolitan area demands)
Policy Issues (3 states)
Agricultural issues (water supply, environmental compliance)
Environmental Issues (water quality, watershed management practices)
Ecological issues (Stream ecosystems, Bird refuge, GSL ecosystem)

## Slide 4: Great Salt Lake
The Great Salt Lake (latitude 40° to 42° N, longitude 112° to 113° W). The effective area of Great Salt Lake basin is about 55,000 km2 .
The study area is divided into five geographic areas (Bear watershed, Weber watershed, Jordan/Provo watershed, West Desert watershed, and Great Salt Lake).
Fresh water inflow comes from Bear (19,262 km2), Weber (6,413 km2), and Jordan/ Provo (9,963 km2) Rivers.

## Slide 5: Great Salt Lake Levels
The lake was divided into North and South arms by a railroad causeway in 1959. Separate records of level in the North Arm and South Arm are available from 1966.
(USGS data)
Feet
Meters
10/15/05 4195.4 ft 1278.8 m
SLC Airport level

## Slide 6: Level-Area-Volume Relationships
(Loving et al., 2000)
Volume (km3)
Area (km2)
Volume (km3)
Level (meter)
Level (meter)
Area (km2)

## Slide 7: Great Salt Lake Volumes
GSL was at its lowest water-surface elevation in recent history at about 1,277.4 m (4,191 ft), it covered about 2,460.5 km2 (950 mi2) and was about 7.6 m deep at its deepest point in 1963.
1987, when Great Salt Lake was at its highest water-surface elevation at about 1,283.8 m (4,212 ft) on April 1st, 1987, it covered about 6,216 km2 (2,400 mi2) and was about 13.7 m at its deepest point.
Acre-Feet  107
km3

## Slide 8: Conceptual Model
Air Humidity
Streamflow
Soil Moisture And Groundwater
Mountain Snowpack
Precipitation
Air Temp.
Evaporation
Solar Radiation
Salinity
GSL Level Volume Area

## Slide 9
Data
Corrine, Bear River
Drainage area 18,205 km2
Plain City, Weber River
Drainage area 5,390 km2
SLC, Jordan/Provo River Drainage area 8,904 km2
Provo, Provo River Drainage area 1,743 km2
Spanish, Jordan River Drainage area 1,689 km2

## Slide 10
Precipitation, Air Temp., Wind speed
Monthly Gridded Precipitation, Air Temperature and Wind Speed over each region from University of Washington (Maurer, E. P., A. W. Wood, J. C. Adam, D. P. Lettenmaier and B. Nijssen, (2002), "A Long-Term Hydrologically Based Dataset of Land Surface Fluxes and States for the Conterminous United States," Journal of Climate, 15: 3237-3251.)

## Slide 11: Spectral Analysis
V+
V-
Log(|A|)
Nov. 1st
June 15th
Biweekly volume (1979-2000)
V km3
Reconstructed GSL Annual cycle - Peak June 15, Trough Nov 1.
Fourier Transform
Month
Notes: When we perform the whole time series we found that the dates are June15, November 15.

## Slide 12: Annual Increase & Decrease
V (+ or -) m3
June 15 - Nov 1
Nov 1 - June 15

## Slide 13: Annual streamflows
m3

## Slide 14: Nov 1 - June 15 lake volume increase
Annual total streamflow, Q (m3)
ΔV+ (m3) Nov 1 - June 15
1:1 line
Lake annual precipitation volume, P (m3)
LOWESS (R defaults)

## Slide 15: Bear River Basin Macro-Hydrology
Streamflow Q/A mm
Precipitation mm
Temperature C
Streamflow response to basin and annual average forcing.
Runoff ratio = 0.18
Runoff ratio = 0.10
LOWESS (R defaults)

## Slide 16: Bear River Basin Macro-Hydrology
Annual Streamflow Q/A mm
SNOTEL Max. SWE mm (average of points)
Temperature C (basin average from gridded data)
SNOTEL Max. SWE mm
LOWESS (R defaults)

## Slide 17: Great Salt Lake Evaporation from annual mass balance E = P+Q-V
Area m2
E m3
LOWESS (R defaults)

## Slide 18: Annual Evaporation Loss E/A
Area m2
E/A m
Salinity decreases as volume increases. E increases as salinity decreases.
LOWESS (R defaults)

## Slide 19: Volume decrease versus E (annual)
E m3
V- m3 June 15 -Nov 1
Significant E in excess of V-. Evaporation not negligible when lake is rising (Nov 1 - June 15)
1:1 line
(from annual mass balance E = P+Q-V)
LOWESS (R defaults)

## Slide 20: Role of salinity (lake surface)
Level m
TDS g/l
Pre 1986
Post 1987
North Arm
South Arm
LOWESS
To a first approx is Salt Load Constant ?

## Slide 21: Total Salt Load (Concentration x Volume)
kg of TDS
Total Load. Sum of North and South arm load.
North arm load.
South arm load.
Salinity inferred from level using LOWESS relationship
South arm observed
North arm observed

## Slide 22: Evaporation vs Salinity
E/A m
C = 3.5 x 1012 kg/(Volume) g/l
Salinity estimated from total load and volume related to decrease in E/A with decrease in lake volume and increase in C
LOWESS (R defaults)

## Slide 23: Evaporation vs Temperature (Annual)
E/A m
Degrees C
LOWESS (R defaults)

## Slide 24: Conclusions
Air Humidity
Streamflow
Soil Moisture And Groundwater
Mountain Snowpack
Precipitation
Air Temp.
Evaporation
Solar Radiation
Salinity
GSL Level Volume Area
Dominant
Reduces
Increases
Area Control
CL/V
Reduces
Contributes
Supplies

## Slide 25: Future and Ongoing Work
Incorporate physical relationship between salinity and vapor pressure into evaporation.
Quantify climate inputs and hydrologic processes separately for the rise (Nov 1 - June 15) and fall (June 15 - Nov 1) periods to refine models.
Integrate the relationships identified into a system model to quantitatively understand the the large scale interactions involved in the dynamics of the Great Salt Lake basin system.
Develop and test predictive capability for quantifying the sensitivity of the GSL system to changes in forcing.