## Slide 1: Modeling the Hydrology of the Great Salt Lake: What makes the Great Salt Lake go up and down
David Tarboton
Utah State University
dtarb@usu.edu
435-797-3172

## Slide 2: Outline
Lake level fluctuations
Water Budget
  Precipitation
  Streamflow
  Evaporation
Sensitivity
Salinity
Modeling
  integrated water and total salt (not individual minerals)

## Slide 3: How a closed basin (e.g. GSL works)
Area, A
Area, A
E x A
Level
Level
Inflows I
I
E x A
If I > E x A level rises
If I < E x A level falls
Level adjusts to fluctuating inputs so that on average
I = E x A
I includes inflows from streams and precipitation on the lake
I = Q + P x A
Subject to climate variability.
E is less variable, but also depends on climate and salinity, C.
As C increases E decreases
Evaporation depth E
Evaporation volume E x A
Volume, V
Salt Load L
Salt Concentration C=L/V

## Slide 5: Water Budget
Q, Streamflow+Groundwater
  3 major rivers. Multiple USGS gauges
  Groundwater 75000 acre ft/yr (Waddell and Barton, 1980)
A, V Area and Volume
  From bathymetry and level
P, Precipitation
  From PRISM (Oregon State University)
E, Evaporation
Withdrawals (West desert pumping, Evaporation ponds)
29%
69%
-96%
-4%
2%

## Slide 6: Bathymetry
South Arm
North Arm
the lake bed topography that relates area to level and volume

## Slide 7: Great Salt Lake Precipitation and Streamflow
Basin | Area (km2) | Precipitation (mm) | Streamflow (acre-ft)
Great Salt Lake | 4713 | 326.7 | -
Bear | 19262 | 536.4 | 1328023 (57%)
Weber | 6413 | 657.4 | 338634 (15%)
Jordan/Provo | 9963 | 563.9 | 509638 (22%)
West Desert | 14604 | 347.7 | -
Other (Davis etc) | - | - | 135240 (6%)
Total | 54953 | 565.6 | 2311434 (100%)
Mean Annual Values 1949-2013
Precipitation from aggregation of PRISM data over each area
Streamflow from multiple USGS gauges

## Slide 8: Great Salt Lake Inputs (1949-2013)
Adjustments to GSL inputs
West Desert pumping. 2.5 MAF removed 4/87 to 6/89. 27 months
200000 AF return from West Desert. 1/90 to 6/92. 30 months
Pond operations 5 months per year May – Sept with withdrawals based on reported water use and water rights.
Precipitation | 991,992 acre-ft (29%)
Streamflow | 2,311,435 acre-ft (69%)
Groundwater | 75,000 acre-ft (2%)
Total Inflows | 3,378,427 acre-ft
Net pumping and withdrawals | -132,060 acre ft (4%)

## Slide 9: Salinity dependent evaporation
(Penman evaporation equation modified for salinity based on ion activity coefficients, Mohammed and Tarboton, 2008)

## Slide 11: What input is the lake level most sensitive to?
Sensitivity
0.3
0.83
0.55
Variability dominated by Q, but stabilized by Ev
But how does Ev depend on area and salinity?
Mohammed, I. N. and D. G. Tarboton, (2012), "An examination of the sensitivity of the Great Salt Lake to changes in inputs," Water Resour. Res., 48(11): W11511, http://dx.doi.org/10.1029/2012WR011908.

## Slide 12: How do changes in area and salinity affect evaporation volume
0.49
0.09
0.07
Variability in evaporation volume is dominated by changes in area with only small effects due to changes in salinity and changes due to potential evaporation

## Slide 13: What about salinity?
North
South
C≈L/V
Causeway Closure
Data from Utah Geological Survey (Andrew Rupke 10/10/2012).

## Slide 14: Calculation of Salt Load
z1, C1
z2, C2
z3, C3
Lake Level h

## Slide 15: Salt Loads
Inferred decline in total dissolved salt in GSL
Data from Utah Geological Survey (Andrew Rupke 10/10/2012). Loads here are reported in US or short tons. 1 US ton = 0.9072 metric tons = 907.2 kg.

## Slide 16: Evaluating the impact of Mineral Evaporation Ponds on Lake Level
Input balanced by less evaporation -> Smaller Area
Bathymetry altered due to Pond occupation of part of Lake
Net effect is a difference in lake level
Time series modeling to account for variability
Smaller Area
Change in level

## Slide 17: Predictive Mass Balance Model
Inputs
  Precipitation (N and S)
  Evaporation (Historic or Calculated)
  Streamflow
  Initial Level
Output
  Levels and volumes
Evaluated separately for N and S arm with Causeway flow by USGS model

## Slide 18: Validation
Note: West desert pumping salt loss reduced to 40% of reported to reconcile with load observations
Notes: GSLFMCausewayModelingHistoric.R

## Slide 19: Validation
Note: West desert pumping salt loss reduced to 40% of reported to reconcile with load observations
Notes: GSLFMCausewayModelingHistoric.R

## Slide 20: Validation
Notes: GSLFMCausewayModelingHistoric.R

## Slide 21: Future simulations
Water budget model with inputs P, Q, E/T resampled from historic years retaining each year as a block
Resampling used k-nearest neighbors (based on total streamflow) to group similar years together and maintain statistical dependence
Evaporation used either the historic value from mass balance, or was calculated from salinity
Pumping limits level to 4208 ft
Pond withdrawal and altered bathymetry scenario

## Slide 22: 100 resampled input simulations
Distribution of 10 year ahead Levels
10 year simulations

## Slide 23: Evaluation of Expansion Pond Alternatives
100 simulated traces of South Arm Level for the no action scenario.
100 simulated traces of South Arm Level for the proposed action scenario
 | South Arm Level |  | 
Quantile | 16% | 50% | 84%
NA | 4190.4 | 4194.1 | 4199.8
PA | 4188.1 | 4192.4 | 4199.0
 | North Arm Concentration (g/L) |  | 
Quantile | 16% | 50% | 84%
NA | 263.8 | 337.6 | 343.8
PA | 239.8 | 332.1 | 341.7
 | North Arm Level |  | 
Quantile | 16% | 50% | 84%
NA | 4189.4 | 4192.8 | 4199.4
PA | 4187.0 | 4190.9 | 4198.7
 | South Arm Concentration (g/L) |  | 
Quantile | 16% | 50% | 84%
NA | 86.9 | 118.4 | 153.6
PA | 80.8 | 119.5 | 151.5
Note: These simulations are from the permit request as of 2010. The permit request has since evolved
10th year quantiles.
Net additional withdrawal 280,000 acre-ft/yr

## Slide 24: Great Salt Lake level predictions time series under different streamflow input change scenarios
Shaded colored areas give the 25th and 75th percentiles for lake level predictions under streamflow changes. Lines give the median (50th percentile) lake level predictions.
Mohammed, I. N. and D. G. Tarboton, (2012), "An examination of the sensitivity of the Great Salt Lake to changes in inputs," Water Resour. Res., 48(11): W11511, http://dx.doi.org/10.1029/2012WR011908.
Notes: Great Salt Lake level predictions time series under different streamflow input change scenarios (25% decrease from annual streamflow input, no streamflow input changes, and 25% increase from annual streamflow input). Shaded colored areas give the 25th and 75th percentiles for lake level predictions under streamflow changes. Lines give the median (50th percentile) lake level predictions.
IF THIS IMAGE HAS BEEN PROVIDED BY OR IS OWNED BY A THIRD PARTY, AS INDICATED IN THE CAPTION LINE, THEN FURTHER PERMISSION MAY BE NEEDED BEFORE ANY FURTHER USE. PLEASE CONTACT WILEY'S PERMISSIONS DEPARTMENT ON PERMISSIONS@WILEY.COM OR USE THE RIGHTSLINK SERVICE BY CLICKING ON THE 'REQUEST PERMISSIONS' LINK ACCOMPANYING THIS ARTICLE. WILEY OR AUTHOR OWNED IMAGES MAY BE USED FOR NON-COMMERCIAL PURPOSES, SUBJECT TO PROPER CITATION OF THE ARTICLE, AUTHOR, AND PUBLISHER.

## Slide 25: Conclusions
Multi-year dynamic variability with 5-10 year adjustment time scale
Streamflow is most sensitive input
Lake area is most sensitive evaporation determinant
Total dissolved salt load is declining
Integrated water and salt simulation effective for addressing questions about future management scenarios
Questions?
dtarb@usu.edu