## Slide 1: Using an Observations Data Model in Hydrologic Information Systems
David G Tarboton
Jeffery S Horsburgh
David R. Maidment
Ilya Zaslavsky
http://www.cuahsi.org/his.html
Support
EAR 0622374

## Slide 2
Databases
Analysis
Models
CUAHSI Hydrologic Information System
Goal: Enhance hydrologic science by facilitating user access to more and better data for testing hypotheses and analyzing processes
Advancement of water science is critically dependent on integration of water information
It is as important to represent hydrologic environments precisely with data as it is to represent hydrologic processes with equations
Rainfall & Snow
Water quantity and quality
Remote sensing
Meteorology
Soil water

## Slide 3: Why an Observations Data Model
Syntactic heterogeneity (File types and formats)
Semantic heterogeneity
  Language for observation attributes (structural)
  Language to encode observation attribute values (contextual)
Publishing and sharing research data
Metadata to facilitate unambiguous interpretation
Enhance analysis capability

## Slide 4: What are the basic attributes to be associated with each single data value and how can these best be organized?
Value
DateTime
Variable
Location
Units
Interval (support)
Accuracy
Offset
OffsetType/ Reference Point
Source/Organization
Censoring
Data Qualifying Comments
Method
Quality Control Level
Sample Medium
Value Type
Data Type

## Slide 5
Data Source
Network
Sites
Variables
Values
{Value, Time, Qualifier, Offset}
Utah State
Univ
Little Bear River
Little Bear River at Mendon Rd
Dissolved Oxygen
9.78 mg/L, 1 October 2007, 6PM
A data source operates an observation network
A network is a set of observation sites
A site is a point location where one or more variables are measured
A variable is a property describing the flow or quality of water
A value is an observation of a variable at a particular time
A qualifier is a symbol that provides additional information about the value
An offset allows specification of measurements at various depths in water
GetSites
GetSiteInfo
GetVariables
GetVariableInfo
GetValues
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment and I. Zaslavsky, (2008), "A Relational Model for Environmental and Water Resources Data," Water Resources Research (in press).
Point Observations Information Model

## Slide 6: CUAHSI Observations Data Model
Streamflow
Flux tower
data
Precipitation
& Climate
Groundwater
levels
Water Quality
Soil
moisture
data
Variables
Space
Time
A relational database at the single observation level (atomic model)
Stores observation data made at points
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Standard format for data sharing
Cross dimension retrieval and analysis

## Slide 7
CUAHSI Observations Data Model
http://www.cuahsi.org/his/odm.html

## Slide 8: Site Attributes
SiteCode, e.g. NWIS:10109000
SiteName, e.g. Logan River Near Logan, UT
Latitude, Longitude Geographic coordinates of site
LatLongDatum Spatial reference system of latitude and longitude
Elevation_m Elevation of the site
VerticalDatum Datum of the site elevation
Local X, Local Y Local coordinates of site
LocalProjection Spatial reference system of local coordinates
PosAccuracy_m Positional Accuracy
State, e.g. Utah
County, e.g. Cache

## Slide 9
Feature
Waterbody
HydroID
HydroCode
FType
Name
AreaSqKm
JunctionID
HydroPoint
HydroID
HydroCode
FType
Name
JunctionID
Watershed
HydroID
HydroCode
DrainID
AreaSqKm
JunctionID
NextDownID
ComplexEdgeFeature
EdgeType
Flowline
Shoreline
HydroEdge
HydroID
HydroCode
ReachCode
Name
LengthKm
LengthDown
FlowDir
FType
EdgeType
Enabled
SimpleJunctionFeature
1
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
*
1
*
HydroNetwork
*
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
1
1
CouplingTable
SiteID
HydroID
Sites
SiteID
SiteCode
SiteName
Latitude
Longitude
…
Observations Data Model
1
1
OR
Independent of, but can be coupled to Geographic Representation
ODM
Arc Hydro

## Slide 10: Variable attributes
VariableName, e.g. discharge
VariableCode, e.g. NWIS:0060
SampleMedium, e.g. water
ValueType, e.g. field observation, laboratory sample
IsRegular, e.g. Yes for regular or No for intermittent
TimeSupport (averaging interval for observation)
DataType, e.g. Continuous, Instantaneous, Categorical
GeneralCategory, e.g. Climate, Water Quality
NoDataValue, e.g. -9999
m3/s
Flow
Cubic meters per second

## Slide 11: Discharge, Stage, Concentration and Daily Average Example

## Slide 12: Stage and Streamflow Example
Notes: Discharge Derived from Gage Height
Concepts:
Data derived from other data – single data point derived from a single observation (discharge from stage)
Data derived using a specific method (discharge from stage using rating curve)
Relationships:
Relationships between Values table and DerivedFrom table on DerivedFromID and ValueID
Relationship between Values table and Variables table on VariableID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID

## Slide 13: Offset
OffsetValue
Distance from a datum or control point at which an observation was made
OffsetType defines the type of offset, e.g. distance below water level, distance above ground surface, or distance from bank of river

## Slide 14: Water Chemistry from a profile in a lake
Notes: Water Chemistry From a Lake Profile
Concepts:
Grouped observations (all observations in one reservoir profile)
Observations made using an offset (observations made at multiple depths below the surface of a reservoir)
Observations made using a specific method (observations made using a particular field instrument)
Relationships:
Relationship between Values table and the Variables table on VariableID
Relationship between Values table and OffestTypes table on OffsetTypeID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID
Relationship between GroupDescriptions table and Groups table on GroupID
Relationship between OffsetTypes table and Units table on UnitID and OffsetUnitID

## Slide 15: Implementation in WATERS Network Information System
11 WATERS Network test bed projects
16 ODM instances (some test beds have more than one ODM instance)
Data from 1246 sites, of these, 167 sites are operated by WATERS investigators
National Hydrologic Information Server
San Diego Supercomputer Center

## Slide 16: Utah – Little Bear River and Mud Lake
Turbidity
Continuous turbidity observations at the Little Bear River at Mendon Road from two different turbidity sensors.

## Slide 17: Florida – Santa Fe Watershed
Nitrate Nitrogen (mg/L)
Millpond Spring
PI: Wendy Graham, ….; DM: Kathleen McKee, Mark Newman

## Slide 18: Loading data into ODM
Interactive OD Data Loader (OD Loader)
  Loads data from spreadsheets and comma separated tables in simple format
Scheduled Data Loader (SDL)
  Loads data from datalogger files on a prescribed schedule.
  Interactive configuration
SQL Server Integration Services (SSIS)
  Microsoft application accompanying SQL Server useful for programming complex loading or data management functions
OD Data Loader
SDL
SSIS

## Slide 19: Managing Data Within ODM - ODM Tools
Query and export – export data series and metadata
Visualize – plot and summarize data series
Edit – delete, modify, adjust, interpolate, average, etc.

## Slide 20
Dynamic controlled vocabulary moderation system
Local ODM
Database
Master ODM Controlled Vocabulary
ODM Website
ODM Controlled
Vocabulary Moderator
ODM Data Manager
ODM
Controlled Vocabulary
Web Services
ODM
Tools
Local
Server
XML
http://water.usu.edu/cuahsi/odm/cv.aspx

## Slide 21: Summary
Syntactic consistency (File types and formats)
Semantic consistency
  Language for observation attributes (structural)
  Language to encode observation attribute values (contextual)
A national network of consistent data
Enhanced data availability
Metadata to facilitate unambiguous interpretation
Enhanced analysis capability

## Slide 22: Future Considerations
Additional data types (grid, image etc.)
Additional catalog sets to enhance discovery
Unit standardization and conversion
Ownership, security, authentication, provenance
Improve controlled vocabulary constraints to enhance integrity

## Slide 23: HIS Website http://www.cuahsi.org/his
Project Team – Introduces members of the HIS Team
Data Access System for Hydrology – Web map interface supporting data discovery and retrieval
Prototype Web Services – WaterOneFlow web services facilitating downlad of time series data from numerous national repositories of hydrologic data
Observations Data Model – Relational database schema for hydrologic observations
HIS Tools – Links to end-user applications developed to support HIS
Documentation and Reports – Status reports, specifications, workbooks and links related to HIS
Feedback – Let us know what you think
Austin Workshop – Material from WATERS workshop in Austin