## Slide 1: Hydrologic Terrain Processing Using Parallel Computing
David Tarboton1, Dan Watson2, Rob Wallace,3 Kim Schreuders1, Teklu Tesfa1
1Utah Water Research Laboratory, Utah State University, Logan, Utah
1Computer Science, Utah State University, Logan, Utah
3US Army Engineer Research and Development Center, Information Technology Lab, Vicksburg, Mississippi
This research was funded by the US Army Research and Development Center under contract number W9124Z-08-P-0420

## Slide 2: Hydrologic Terrain Analysis
Raw DEM
Sink Removal
Flow Field
Flow Related Terrain Information
to derive hydrologic information, and inputs to hydrologic models from digital elevation data

## Slide 3: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 4: A parallel version of the TauDEM Software Tools
Improved runtime efficiency
Capability to run larger problems
Platform independence of core functionality

## Slide 5: Parallel Approach
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 6: Pit Removal: Planchon Fill Algorithm
Initialization
1st Pass
2nd Pass
Planchon, O., and F. Darboux (2001), A fast, simple and versatile algorithm to fill the depressions of digital elevation models, Catena(46), 159-176.

## Slide 7: Parallel Scheme
Communicate
Initialize( Z,F) Do for all grid cells i if Z(i) > n F(i) ← Z(i) Else F(i) ← n i on stack for next pass endfor Send( topRow, rank-1 ) Send( bottomRow, rank+1 ) Recv( rowBelow, rank+1 ) Recv( rowAbove, rank-1 ) Until F is not modified
Z denotes the original elevation.
F denotes the pit filled elevation.
n denotes lowest neighboring elevation
i denotes the cell being evaluated
Iterate only over stack of changeable cells

## Slide 8: Parallel Pit Remove Timing GSL100 (4045 x 7402 = 29.9 x 106 cells  120 MB)
Dual Quad Core Xeon Proc E5405, 2.00GHz

## Slide 9: Parallel Pit Remove Stack vs Domain Iteration Timing GSL100 (4045 x 7402 = 29.9 x 106 cells  120 MB)
Dual Quad Core Xeon Proc E5405, 2.00GHz
it is important to limit iteration to unresolved grid cells

## Slide 10: Parallel Pit Remove Block vs Cell IO Timing GSL100 (4045 x 7402 = 29.9 x 106 cells  120 MB)
Dual Quad Core Xeon Proc E5405, 2.00GHz
it is important to use block IO

## Slide 11: Parallel Pit Remove Timing NEDB (14849 x 27174 = 4 x 108 cells  1.6 GB)
Dual Quad Core Xeon Proc E5405, 2.00GHz

## Slide 12: Representation of Flow Field
D
D8
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 13: Pseudocode for Recursive Flow Accumulation
FlowAccumulation(i) for all k neighbors of i if Pki>0 FlowAccumulation(k) next k return
Pki
Pki
Pki
i
i = FA(i, Pki, k, k)
or generalized flow algebra

## Slide 14
Used to evaluate Contributing Area

## Slide 15: Or extended to more general concepts such as retention limited runoff generation with run-on
FlowAlgebra(i) for all k neighbors of i if Pki>0 FlowAlgebra(k) next k return
r
c
qi
qk

## Slide 16: and decaying accumulation
Useful for a tracking contaminant or compound movement subject to decay or attenuation

## Slide 17: Parallelization of Contributing Area/Flow Algebra
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-2
Queue’s empty so exchange border info.
B=-1
A=1
A=1
A=1
D=0
A=3
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-2
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
D=0
D=0
A=1
D=1
D=1
resulting in new D=0 cells on queue
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
A=5.5
A=2.5
A=1
A=6
A=3.5
and so on until completion
A=1
A=1
A=1
D=0
D=0
D=0
A=1
D=2
D=1
A=1
D=1
D=1
D=0
D=0
D=0
D=1
D=3
D=1
D=0
D=2
D=1
D=0
D=3
D=1
A=1
D=0
D=0
D=1
D=2
D=0
A=1
D=2
D=1
D=0
D=2
D=1
A=1
A=1
D=0
D=1
D=1
D=0
A=1
D=2
D=1
A=1
D=1
D=1
A=1
A=1
A=1
D=1
D=0
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-1
Decrease cross partition dependency
Executed by every process with grid flow field P, grid dependencies D initialized to 0 and an empty queue Q. FindDependencies(P,Q,D) for all i for all k neighbors of i if Pki>0 D(i)=D(i)+1 if D(i)=0 add i to Q next
Executed by every process with D and Q initialized from FindDependencies. FlowAlgebra(P,Q,D,,) while Q isn’t empty get i from Q i = FA(i, Pki, k, k) for each downslope neighbor n of i if Pin>0 D(n)=D(n)-1 if D(n)=0 add n to Q next n end while swap process buffers and repeat
1. Dependency grid
2. Flow algebra function

## Slide 18: D-infinity Contributing Area Timing GSL100 (4045 x 7402 = 29.9 x 106 cells  120 MB)
Dual Quad Core Xeon Proc E5405, 2.00GHz

## Slide 19: D-infinity Contributing Area Timing Boise River (24856 x 24000 = 5.97 x 108 cells  2.4 GB)
Dual Quad Core Xeon Proc E5405, 2.00GHz

## Slide 20: Limitations and Dependencies
Uses MPICH2 library from Argonne National Laboratory http://www.mcs.anl.gov/research/projects/mpich2/
TIFF (GeoTIFF) 4 GB file size
[Capability to use BigTIFF and tiled files under development.]
Processor memory

## Slide 21: Conclusions
Parallelization speeds up processing and partitioned processing reduces size limitations
Parallel logic developed for general recursive flow accumulation methodology (flow algebra)
New toolbox allows use within model builder
Methods and software soon to be available in TauDEM at: http://www.engineering.usu.edu/dtarb